HALOE STANDARD HEADER CONTENTS For Version 19 delivery

This is the standard header for Level 2 files.

| Position | Name | Contents |
| --- | --- | --- |
| 1 | LABEL | CHARACTER*10 label showing type of header See HDTYP below |
| 2 | NHEAD | Size in REAL*4 words for this header (INTEGER*4) Currently 120 for Level 1 (NHDLEV = 7) Currently 127 for Level 2 (NHDLEV = 19) |
| 3 | NHDLEV | The generation of the file. (INTEGER*4) Changes in the structure of the file will cause a change in this number. Currently NHDLEV = 8 for Level 1 Currently NHDLEV = 19 for Level 2 |
| 4 | HDTYP | Header type (INTEGER*4). 2 = LEVEL 2 standard 'STD_L2 ' Level 2 |
| 5 | HEAD (NHEAD) | Header values (REAL*4) |

| Position IN HEAD | Name | Contents |
| --- | --- | --- |
| 1 | DATES | date for start of track data (UDTF) INTEGER*4 |
| 2 | TIMES | time for start of track data (UDTF) INTEGER*4 |
| 3 | DATEE | date for end of track data (UDTF) INTEGER*4 |
| 4 | TIMEE | time for end of track data (UDTF) INTEGER*4 |
| 5 | MODE | track mode indicator (8=SET, 10=RISE) INTEGER*4 |
| 6 | NEVENT | event number ( -1 for average events ) INTEGER*4 |
| 7 | SANG | apparent zenith angle for 1st data point (radians) when HDTYP = 11. apparent zenith angle for 1st data point (radians) relative to top edge of sun when HDTYP = 12. not applicable for HDTYP = 13. |
| 8 | AINC | angle increment between points data points (radians) not applicable for HDTYP = 13. |
| 9 | SZ | apparent tangent altitude for 1st point (km) not applicable for HDTYP = 12 or HDTYP = 13. |
| 10 | ZINC | apparent tangent altitude increment (km) not applicable for HDTYP = 12 or HDTYP = 13. |
| 11 | NPTS | number of data samples INTEGER*4 number of registration points when HDTYP = 11 number of solar scan points when HDTYP = 12 not applicable when HDTYP = 13 |
| 12 | NRCRDS | number of records INTEGER*4 not applicable for LEVEL 1 headers. |
| 13 | IORB | uars orbit number INTEGER*4 |
| 14 | SALT | spacecraft altitude (km) at TIMES |
| 15 | SLAT | spacecraft latitude (degrees) at TIMES |
| 16 | SLON | spacecraft longitude (degrees) at TIMES |
| 17-28 | NERROR(12) | number of error occurrences for each channel INTEGER*4 |
| 29-40 | EXOSIG(12) | exoatmospheric signals for each channel (Volts) |
| 41-52 | SIGVAL(12) | one sigma value (arcminutes) for gaussian apodization function for each channel. |
| 53 | ERAD90 | earth radius (km) for subtangent point of 90 km tangent altitude ray |
| 54 | ERAD30 | earth radius (km) for subtangent point of 30 km tangent altitude ray |
| 55 | ERAD6 | earth radius (km) for subtangent point of 6 km tangent altitude ray |
| 56-59 | DxxxT | average detector housing temperatures (K) for: CO2, H2O, NO2, & O3 |
| 60-63 | SDxxxT(4) | standard deviation of detector housing temperatures (K) |
| 64-67 | xxxFLT(4) | average spectral filter temperatures (K) for: CH4, HCl, NO, & HF |
| 68-71 | SxxxFLT(4) | standard deviation of spectral filter temperatures (K) |
| 72-75 | GCTxxx(4) | average gas cell temperature indicators (K): MFMT, MFCAT, GCRT, & HFGCT (CH4, HCL, NO, HF) |
| 76-79 | SGCTxxx(4) | standard deviation of cell temperature indicators (K) |
| 80 | BETA | beta angle (deg) |
| 81 | STLAT | latitude (degrees) for 150 km subtangent point HDTYP = 2 ONLY |
| 82 | STLON | longitude (degrees) for 150 km subtangent point HDTYP = 2 ONLY |
| 83 | ETLAT | latitude (degrees) for 3 km subtangent point HDTYP = 2 ONLY |
| 84 | ETLON | longitude (degrees) for 3 km subtangent point HDTYP = 2 ONLY |
| 85 | EVNLAT | latitude (degrees) for 30 km subtangent point HDTYP = 2 ONLY |
| 86 | EVNLON | longitude (degrees) for 30 km subtangent point HDTYP=2 ONLY |
| 87 | EVNVELS | S/C velocity relative to the sun for the 30 km tangent ray (km/sec) HDTYP = 2 ONLY |
| 88 | EVNVELA | S/C velocity relative to the atm for the 30 km tangent ray (km/sec) HDTYP = 2 ONLY |
| 89-90 | METH(4) | endo/exo atmospheric and measure/calculated V code for the gas filter channels: NO, CH4 (CH4 DV), HCL, & HF HDTYP = 2 ONLY INTEGER*2 |
| 91 | MSISFLAG | indicates if MSIS model was used to determine high altitude Temperature profile INTEGER*4 1 = MSIS model used for temperature determination 0 = MSIS model not used. not applicable for HDTYP = 12 or HDTYP = 13 |
| 92 | CH4_SAT_Z | The altitude where the CH4DV channel saturates (km) REAL*4 HDTYP = 2 ONLY |
| 93 | CH4_SAT_P | The pressure at the altitude where the CH4DV channel saturates (mb) REAL*4 HDTYP = 2 ONLY |
| 94 | ALT_GAIN | The apparent where the fine sun sensor on the instrument changes its Gain value (km) |
| 95 | Z_CIRRUS | Altitude of Cirrus Tops, if detected (km) HDTYP=2 ONLY |
| 96 | MCH4 | CH4 Merged Technique HDTYP=2 ONLY INTEGER*4 |
| 97 | EVNSTAT | status flag for this event HDTYP = 2 ONLY INTEGER*4 0 = skipped event i.e. level 1 data only 1 = level 1 data and level 2 data |
| 98 | PTFLAG | defines data used to generate pressure registration INTEGER*4 not applicable for HDTYP = 12 or HDTYP = 13 = 0 if NMC data used = 1 if UKMO data used |
| 99-104 | SMOOTH(12) | index for vertical smoothing HDTYP = 2 ONLY (INTEGER*2) |
| 105-110 | INDAERO(12) | index for aerosol model HDTYP = 2 ONLY (INTEGER*2) |
| 111 | ALTLOW | lower range of valid data (km) HDTYP=2 ONLY |
| 112 | ALTHIGH | high range of valid data (km) HDTYP=2 ONLY |
| 113 | BOTEXC | number of diodes exceeded when track was lost HDTYP=2 ONLY |
| 114 | SOLEXTLO | solar extent at ALTLOW (arcmin) HDTYP=2 ONLY |
| 115 | APPTOPLO | altitude of the apparent top edge of the sun at ALTLOW (km) HDTYP=2 ONLY |
| 116 | ZA_OFF_SUN | altitude at which FOV starts to slide off bottom of the sun (km) HDTYP=2 ONLY |
| 117 | ZTROP | tropopause altitude (km) HDTYP=2 ONLY |
| 118 | PTROP | pressure at ZTROP (mb) HDTYP=2 ONLY |
| 119 | TTROP | temperature at ZTROP (K) HDTYP=2 ONLY |
| 120-127 | IDIFLAG(16) | NOx and O3 diurnal gradient indicator for each channel: CO2, H2O, NO2, O3, NO, CH4 DV, CH4 (HCL V), CH4 V, HCL, HF HFV NOAERO CH4AERO HCLAERO HFAERO HDTYP=2 ONLY INTEGER*2 |

NOTES:	All values are REAL*4 unless otherwise indicated. To access the integers you must read the header as a REAL*4 array and then equivalence the proper HEAD elements to INTEGER variables.

This is the format of the LEVEL 2 data. The top of the data file has the following SFDU etc headers:

LEVEL 2 SFDU HEADERS AND DAILY SUMMARY (VERSION 3)

--------------------------------------------------

| RECORD | CONTENTS |
| --- | --- |
| 1 | SFDU Header CHARACTER*72 "CCSD1Z00000100000052CCSD1R00000300000032DELIMITER =EOF;TYPY=NURS1I00HA02;" |
| 2 | CHFH, NWORDS, NHDLEV2, NHEAD CHFH CHARACTER*10, Character descripter of this record NWORDS Number of elements that follow INTEGER*4 NHDLEV2 Level 2 file generation number INTEGER*4 NHEAD Number of values in the level 2 header INTEGER*4 |
| 3 | CHFH, NCOM,(COMMENT(I),I=1,NCOM) CHFH CHARACTER*10, Character descripter of this record NCOM Number of comments that follow INTEGER*4 COMMENT Comments describing the file CHARACTER*80 |
| 4 | CHFH, NWORDS, UARS_DAY, NL1EVNTS, NRET, NSKIPPED CHFH CHARACTER*10, Character descripter of this record NWORDS Number of elements that follow INTEGER*4 UARS_DAY UARS Day INTEGER*4 NL1EVENTS Number of events in the level 1 file INTEGER*4 NRET Number of events retrieved. INTEGER*4 NSKIP Number of events skipped INTEGER*4 |
| 5 | CHFH, NWORDS, (NSKIPPED(I),I=1,NWORDS) CHFH CHARACTER*10, Character descripter of this record NWORDS Number of elements that follow INTEGER*4 NSKIPPED Array of skipped events INTEGER*4 NSKIPPED(2)=0 Means event #2 was processed NSKIPPED(2)=2 Means event #2 was skipped |
| 6 | CHFH, NWORDS, AVGLAT_SS, AVGVELS_SS, AVGVELA_SS CHFH CHARACTER*10, Character descripter of this record NWORDS Number of elements that follow INTEGER*4 AVGLAT_SS Average 30 km TPA latitude for SS events (deg) REAL*4 AVGVELS_SS Average 30 km TPA S/C velocity relative to the sun for SS events (km/sec) REAL*4 AVGVELS_SS Average 30 km TPA S/C velocity relative to the atmosphere for SS events (km/sec) REAL*4 |
| 7 | CHFH, NWORDS, AVGLAT_SR, AVGVELS_SR, AVGVELA_SR CHFH CHARACTER*10, Character descripter of this record NWORDS Number of elements that follow INTEGER*4 AVGLAT_SR Average 30 km TPA latitude for SS events (deg) REAL*4 AVGVELS_SR Average 30 km TPA S/C velocity relative to the sun for SR events (km/sec) REAL*4 AVGVELS_SR Average 30 km TPA S/C velocity relative to the atm for SR events (km/sec) REAL*4 |
| 8 | CHFH, NWORDS, (EVNT_TYPE(I),I=1,NWORDS) CHFH CHARACTER*10, Character descripter of this record NWORDS Number of elements that follow INTEGER*4 EVNT_TYPE Event type of each event used for summary data CHARACTER*10 |
| 9 | CHFH, NWORDS, (SUM_LAT(I),I=1,NWORDS) CHFH CHARACTER*10, Character descripter of this record NWORDS Number of elements that follow INTEGER*4 SUM_LAT 30 km TPA latitudes for each summary event (degrees) REAL*4 |
| 10 | CHFH, NWORDS, (SUM_LON(I),I=1,NWORDS) CHFH CHARACTER*10, Character descripter of this record NWORDS Number of elements that follow INTEGER*4 SUM_LON 30 km TPA longitudes for each summary event (degrees) REAL*4 |
| 11 | CHFH, NWORDS, (SUM_VELS(I),I=1,NWORDS) CHFH CHARACTER*10, Character descripter of this record NWORDS Number of elements that follow INTEGER*4 SUM_VELS 30 km TPA S/C velocity relative to the sun for each summary event (km/sec) REAL*4 |
| 12 | CHFH, NWORDS, (SUM_VELA(I),I=1,NWORDS) CHFH CHARACTER*10, Character descripter of this record NWORDS Number of elements that follow INTEGER*4 SUM_VELA 30 km TPA S/C velocity relative to the atmosphere for each summary event (km/sec) REAL*4 |
| 13 | CHFH, NWORDS CHFH CHARACTER*10, Last record NWORDS Number of elements that follow INTEGER*4 |

--------------------------------------------------------------------------

The following will be output for each event

| RECORD |  |
| --- | --- |
| 1 | standard header (LABEL = 'STD_L2 ' HDTYP = 2) LABEL, NHEAD, NHDLEV, HDTYP, (HEAD(I),I=1,NHEAD) |
| 2 to NRCRDS+1 CHAR_LABEL, INDEX, NUM, (ARRAY(I),I=1,NUM) |
|  | CHARACTER*10 CHAR_LABEL Data array descriptor INTEGER*4 INDEX Unique index for this data array INTEGER*4 NUM Number of elements that follow REAL*4 ARRAY(NUM) Data values [except for the records with SMTON, SMTF, and IFILT, which are INTEGER*4 instead] |
|  | NOTE: that the order in which the data is output to the level 2 file is not in the following order or in the INDEX order. You must read in all NRCRDS of data and reference the data via its INDEX number If NUM=0 then no data exist in the array. |

| INDEX | CONTENTS | LABEL |
| --- | --- | --- |
| 1 | apparent tangent altitudes (km) | 'APPTANALT ' |
| 9 | apparent tangent altitude pressures from NMC (mb) NOTE: this is UKMO data if PTFLAG =1 | 'PRAPPTNZ ' |
| 10 | apparent tangent altitude temperatures from NMC (K) NOTE: this is UKMO data if PTFLAG =1 | 'TEMAPPTNZ ' |
| 3 | apparent subtangent point latitudes (deg) | 'APPTANLAT ' |
| 4 | apparent subtangent point longitudes (deg) | 'APPTANLON ' |
| 126 | UKMO pressures for each apparent altitude (mb) NOTE: this NMC data if PTFLAG =1 | 'UKMOPR ' |
| 127 | UKMO temperatures for each apparent altitude (K) NOTE: this is NMC data if PTFLAG = 1 | 'UKMOTEMP ' |
| 2 | zenith angles for each apparent altitude (radians) | 'APPZENANG ' |
| 201 | acceleration of gravity for each apparent tangent altitude (m/s/s) | 'GRAV_ACC ' |
| 206 | refraction angle for each apparent tangent altitude (radians) | 'REFRAC ' |
| 204 | apparent solar extent for each apparent tangent altitude (radians) | 'SOLEXT ' |
| 205 | apparent altitude of the Sun's top edge for each apparent tangent altitude (km) | 'APPTOPY ' |
| 5 | elapsed time since start of event for each apparent altitude (seconds) | 'TIMES ' |
| 11 | position of the center of the instrument boresight on the solar disk for each elapsed time (radians down from the top edge) | 'FSSPOS ' |
| 202 | gimble elevation angles for each elapsed time (radians) | 'GIMBLE ' |
| 203 | gimble zenith angles for each elapsed time (radians) | 'GIMBLZ ' |
| 207 | spacecraft subtangent latitude for each elapsed time (deg) | 'SCLATS ' |
| 208 | spacecraft subtangent longitude for each elapsed time (deg) | 'SCLONS ' |
| 223 | spacecraft altitude for each elapsed time (km) | 'SCALTS ' |
| 224 | Instrument VPEAK signal (units???) | 'VPEAK ' |
| 225 | Boresight correction using the VPEAK signal (units???) | 'VPCOR ' |
| 6 | spacecraft velocity relative to the sun for each elapsed time (km/s along line of sight). >0 is increasing separation distance | 'LOSVELSUN ' |
| 7 | spacecraft velocity relative to the apparent tangent point for each elapsed time (km/s along line of sight) >0 is increasing separation distance | 'LOSVELATM ' |
| 159 | CO2 boresight position on the solar disk for each apparent altitude (radians down from the top edge) | 'LINTCO2 ' |
| 160 | H2O boresight position on the solar disk for each apparent altitude (radians down from the top edge) | 'LINTH2O ' |
| 161 | NO2 boresight position on the solar disk for each apparent altitude (radians down from the top edge) | 'LINTNO2 ' |
| 162 | O3 boresight position on the solar disk for each apparent altitude (radians down from the top edge) | 'LINTO3 ' |
| 163 | CH4 boresight position on the solar disk for each apparent altitude (radians down from the top edge) | 'LINTCH4 ' |
| 164 | CH4D boresight position on the solar disk for each apparent altitude (radians down from the top edge) | 'LINTCH4D ' |
| 165 | HCL boresight position on the solar disk for each apparent altitude (radians down from the top edge) | 'LINTHCL ' |
| 166 | HCLD boresight position on the solar disk for each apparent altitude (radians down from the top edge) | 'LINTHCLD ' |
| 167 | NO boresight position on the solar disk for each apparent altitude (radians down from the top edge) | 'LINTNO ' |
| 168 | NOD boresight position on the solar disk for each apparent altitude (radians down from the top edge) | 'LINTNOD ' |
| 169 | HF boresight position on the solar disk for each apparent altitude (radians down from the top edge) | 'LINTHF ' |
| 170 | HFD boresight position on the solar disk for each apparent altitude (radians down from the top edge) | 'LINTHFD ' |
| 12 | CO2 signal at each apparent altitude (volts) | 'INTCO2 ' |
| 13 | H2O signal at each apparent altitude (volts) | 'INTH2O ' |
| 14 | NO2 signal at each apparent altitude (volts) | 'INTNO2 ' |
| 15 | O3 signal at each apparent altitude (volts) | 'INTO3 ' |
| 16 | CH4 signal at each apparent altitude (volts) | 'INTCH4 ' |
| 17 | CH4 difference signal at each apparent altitude (volts) | 'INTDCH4 ' |
| 18 | HCL signal at each apparent altitude (volts) | 'INTHCL ' |
| 19 | HCL difference signal at each apparent altitude (volts) | 'INTDHCL ' |
| 20 | NO signal at each apparent altitude (volts) | 'INTNO ' |
| 21 | NO difference signal at each apparent altitude (volts) | 'INTDNO ' |
| 22 | HF signal at each apparent altitude (volts) | 'INTHF ' |
| 23 | HF difference signal at each apparent altitude (volts) | 'INTDHF ' |
| 155 | SMTON, 1 if channel J is filtered | 'SMTON ' |
| 156 | SMTF, noise reduction factor for channel J | 'SMTF ' |
| 157 | SMTP, noise/signal desired for channel J | 'SMTP ' |
| 158 | IFILT(1:12) SMOOTHING FOR CHANNEL: 1 IF SMOOTHED and 0 IF NO SMOOTHING | 'IFILT ' |
| 24 | Normalized CO2V solar limb darkening curve | 'LDCO2 ' |
| 25 | Normalized H2OV solar limb darkening curve | 'LDH2O ' |
| 26 | Normalized NO2V solar limb darkening curve | 'LDNO2 ' |
| 27 | Normalized O3V solar limb darkening curve | 'LDO3 ' |
| 28 | Normalized CH4V solar limb darkening curve | 'LDCH4 ' |
| 29 | Normalized HCLV solar limb darkening curve | 'LDHCL ' |
| 30 | Normalized NOV solar limb darkening curve | 'LDNO ' |
| 31 | Normalized HFV solar limb darkening curve | 'LDHF ' |
| 173 | Normalized CH4DV solar limb darkening curve | 'LDDCH4 ' |
| 174 | Normalized HCLDV solar limb darkening curve | 'LDDHCL ' |
| 175 | Normalized NODV solar limb darkening curve | 'LDDNO ' |
| 176 | Normalized HFDV solar limb darkening curve | 'LDDHF ' |
| 177 | Residual difference limb darkening curve CO2V | 'DLDCO2 ' |
| 178 | Residual difference limb darkening curve H2OV | 'DLDH2O ' |
| 179 | Residual difference limb darkening curve NO2V | 'DLDNO2 ' |
| 180 | Residual difference limb darkening curve O3V | 'DLDO3 ' |
| 181 | Residual difference limb darkening curve CH4V | 'DLDCH4 ' |
| 182 | Residual difference limb darkening curve CH4DV | 'DLDCH4D ' |
| 183 | Residual difference limb darkening curve HCLV | 'DLDHCL ' |
| 184 | Residual difference limb darkening curve HCLDV | 'DLDHCLD ' |
| 185 | Residual difference limb darkening curve NOV | 'DLDNO ' |
| 186 | Residual difference limb darkening curve NODV | 'DLDNOD ' |
| 187 | Residual difference limb darkening curve HFV | 'DLDHF ' |
| 188 | Residual difference limb darkening curve HFDV | 'DLDHFD ' |
| 171 | RMS Error for each channel of the DLDXXX array | 'ELD ' |
| 172 | Max Error for each channel of the DLDXXX array | 'EMLD ' |
| 189 | CO2 sunspot residual in noise units for channel | 'SPOTCO2 ' |
| 190 | H2O sunspot residual in noise units for channel | 'SPOTH2O ' |
| 191 | NO2 sunspot residual in noise units for channel | 'SPOTNO2 ' |
| 192 | O3 sunspot residual in noise units for channel | 'SPOTO3 ' |
| 193 | CH4 sunspot residual in noise units for channel | 'SPOTCH4 ' |
| 194 | CH4DV sunspot residual in noise units for channel | 'SPOTCH4D ' |
| 195 | HCL sunspot residual in noise units for channel | 'SPOTHCL ' |
| 196 | HCLDV sunspot residual in noise units for channel | 'SPOTHCLD ' |
| 197 | NO sunspot residual in noise units for channel | 'SPOTNO ' |
| 198 | NODV sunspot residual in noise units for channel | 'SPOTNOD ' |
| 199 | HF sunspot residual in noise units for channel | 'SPOTHF ' |
| 200 | HFDV sunspot residual in noise units for channel | 'SPOTHFD ' |
| 139 | Off-Sun offset (volts) in order below CO2, H2O, NO2, O3, CH4, DCH4, HCL, DHCL, NO, DNO, HF, DHF | 'OFFSUN ' |
| 32 | CO2 (PRESS/TEMP) RETRIEVAL: PRESSURE (mb) | 'PRCO2 ' |
| 33 | CO2 (PRESS/TEMP) RETRIEVAL: ALTITUDE (km) | 'ALTCO2 ' |
| 34 | CO2 (PRESS/TEMP) RETRIEVAL: TEMPERATURE (K) | 'TEMPCO2 ' |
| 35 | CO2 (PRESS/TEMP) RETRIEVAL: VOLUME MIXING RATIO | 'XMIXCO2 ' |
| 36 | CO2 (PRESS/TEMP) RETRIEVAL: QUALITY PROFILES | 'QUALCO2 ' |
| 128 | CO2 (PRESS/TEMP) RETRIEVAL: RETRIEVAL FLAG | 'RFLGCO2 ' |
| 37 | CO2 (PRESS/TEMP) RETRIEVAL: AEROSOL TRANSMISSION | 'ATRANCO2 ' |
| 38 | CO2 (PRESS/TEMP) RETRIEVAL: AEROSOL EXTINCTION (1/km) | 'AEXCO2 ' |
| 39 | CO2 (PRESS/TEMP) RETRIEVAL: COLUMN SUM (molec/sq.cm) | 'CO2 CS ' |
| 140 | CO2 (PRESS/TEMP) RETRIEVAL: REFRACTION FACTOR | 'RF CO2 ' |
| 40 | H2O RETRIEVAL: PRESSURE (mb) | 'PRH2O ' |
| 41 | H2O RETRIEVAL: ALTITUDE (km) | 'ALTH2O ' |
| 42 | H2O RETRIEVAL: TEMPERATURE (K) | 'TEMPH2O ' |
| 43 | H2O RETRIEVAL: VOLUME MIXING RATIO | 'XMIXH2O ' |
| 44 | HO RETRIEVAL: QUALITY PROFILES | 'QUALH2O ' |
| 129 | H2O RETRIEVAL: RETRIEVAL FLAG | 'RFLGH2O ' |
| 45 | H2O RETRIEVAL: AEROSOL TRANSMISSION | 'ATRANH2O ' |
| 46 | H2O RETRIEVAL: AEROSOL EXTINCTION (1/km) | 'AEXH2O ' |
| 138 | H2O RETRIEVAL: COLUMN SUM (molec/sq.cm) | 'H2O CS ' |
| 141 | H2O RETRIEVAL: REFRACTION FACTOR | 'RF H2O ' |
| 48 | NO2 RETRIEVAL: PRESSURE (mb) | 'PRNO2 ' |
| 49 | NO2 RETRIEVAL: ALTITUDE (km) | 'ALTNO2 ' |
| 50 | NO2 RETRIEVAL: TEMPERATURE (K) | 'TEMPNO2 ' |
| 51 | NO2 RETRIEVAL: VOLUME MIXING RATIO | 'XMIXNO2 ' |
| 52 | NO2 RETRIEVAL: QUALITY PROFILES | 'QUALNO2 ' |
| 130 | NO2 RETRIEVAL: RETRIEVAL FLAG | 'RFLGNO2 ' |
| 53 | NO2 RETRIEVAL: AEROSOL TRANSMISSION | 'ATRANNO2 ' |
| 54 | NO2 RETRIEVAL: AEROSOL EXTINCTION (1/km) | 'AEXNO2 ' |
| 55 | NO2 RETRIEVAL: COLUMN SUM (molec/sq.cm) | 'NO2 CS ' |
| 142 | NO2 RETRIEVAL: REFRACTION FACTOR | 'RF NO2 ' |
| 56 | O3 RETRIEVAL: PRESSURE (mb) | 'PRO3 ' |
| 57 | O3 RETRIEVAL: ALTITUDE (km) | 'ALTO3 ' |
| 58 | O3 RETRIEVAL: TEMPERATURE (K) | 'TEMPO3 ' |
| 59 | O3 RETRIEVAL: VOLUME MIXING RATIO | 'XMIXO3 ' |
| 60 | O3 RETRIEVAL: QUALITY PROFILES | 'QUALO3 ' |
| 131 | O3 RETRIEVAL: RETRIEVAL FLAG | 'RFLGO3 ' |
| 61 | O3 RETRIEVAL: AEROSOL TRANSMISSION | 'ATRANO3 ' |
| 62 | O3 RETRIEVAL: AEROSOL EXTINCTION (1/km) | 'AEXO3 ' |
| 63 | O3 RETRIEVAL: COLUMN SUM (molec/sq.cm) | 'O3 CS ' |
| 143 | O3 RETRIEVAL: REFRACTION FACTOR | 'RF O3 ' |
| 64 | NO RETRIEVAL: PRESSURE (mb) | 'PRNO ' |
| 65 | NO RETRIEVAL: ALTITUDE (km) | 'ALTNO ' |
| 66 | NO RETRIEVAL: TEMPERATURE (K) | 'TEMPNO ' |
| 67 | NO RETRIEVAL: VOLUME MIXING RATIO | 'XMIXNO ' |
| 68 | NO RETRIEVAL: QUALITY PROFILES | 'QUALNO ' |
| 132 | NO RETRIEVAL: RETRIEVAL FLAG | 'RFLGNO ' |
| 69 | NO RETRIEVAL: AEROSOL TRANSMISSION | 'ATRANNO ' |
| 70 | NO RETRIEVAL: AEROSOL EXTINCTION (1/km) | 'AEXNO ' |
| 71 | NO RETRIEVAL: COLUMN SUM (molec/sq.cm) | 'NO CS ' |
| 144 | NO RETRIEVAL: REFRACTION FACTOR | 'RF NO ' |
| 72 | DCH4 RETRIEVAL: PRESSURE (mb) | 'PRDCH4 ' |
| 73 | DCH4 RETRIEVAL: ALTITUDE (km) | 'ALTDCH4 ' |
| 74 | DCH4 RETRIEVAL: TEMPERATURE (K) | 'TEMPDCH4 ' |
| 75 | DCH4 RETRIEVAL: VOLUME MIXING RATIO | 'XMIXDCH4 ' |
| 76 | DCH4 RETRIEVAL: QUALITY PROFILES | 'QUALDCH4 ' |
| 133 | DCH4 RETRIEVAL: RETRIEVAL FLAG | 'RFLGDCH4 ' |
| 77 | DCH4 RETRIEVAL: AEROSOL TRANSMISSION | 'ATRANDCH4 ' |
| 78 | DCH4 RETRIEVAL: AEROSOL EXTINCTION (1/km) | 'AEXDCH4 ' |
| 79 | DCH4 RETRIEVAL: COLUMN SUM (molec/sq.cm) | 'DCH4 CS ' |
| 145 | DCH4 RETRIEVAL: REFRACTION FACTOR | 'RF DCH4 ' |
| 80 | CH4 (HCL V) RETRIEVAL: PRESSURE (mb) | 'PRCH4HCL ' |
| 81 | CH4 (HCL V) RETRIEVAL: ALTITUDE (km) | 'ALTCH4HCL ' |
| 82 | CH4 (HCL V) RETRIEVAL: TEMPERATURE (K) | 'TEMPCH4HCL' |
| 83 | CH4 (HCL V) RETRIEVAL: VOLUME MIXING RATIO | 'XMIXCH4HCL' |
| 84 | CH4 (HCL V) RETRIEVAL: QUALITY PROFILES | 'QUALCH4HCL' |
| 134 | CH4 (HCL V) RETRIEVAL: RETRIEVAL FLAG | 'RFLGCH4HCL' |
| 85 | CH4 (HCL V) RETRIEVAL: AEROSOL TRANSMISSION | 'ATRANCH4HCL' |
| 86 | CH4 (HCL V) RETRIEVAL: AEROSOL EXTINCTION (1/km) | 'AEXCH4HCL ' |
| 87 | CH4 (HCL V) RETRIEVAL: COLUMN SUM (molec/sq.cm) | 'CH4HCL CS ' |
| 146 | CH4 (HCL V) RETRIEVAL: REFRACTION FACTOR | 'RF CH4HCL ' |
| 88 | CH4 RETRIEVAL: PRESSURE (mb) | 'PRCH4 ' |
| 89 | CH4 RETRIEVAL: ALTITUDE (km) | 'ALTCH4 ' |
| 90 | CH4 RETRIEVAL: TEMPERATURE (K) | 'TEMPCH4 ' |
| 91 | CH4 RETRIEVAL: VOLUME MIXING RATIO | 'XMIXCH4 ' |
| 92 | CH4 RETRIEVAL: QUALITY PROFILES | 'QUALCH4 ' |
| 135 | CH4 RETRIEVAL: RETRIEVAL FLAG | 'RFLGCH4 ' |
| 93 | CH4 RETRIEVAL: AEROSOL TRANSMISSION | 'ATRANCH4 ' |
| 94 | CH4 RETRIEVAL: AEROSOL EXTINCTION (1/km) | 'AEXCH4 ' |
| 95 | CH4 RETRIEVAL: COLUMN SUM (molec/sq.cm) | 'CH4 CS ' |
| 147 | CH4 RETRIEVAL: REFRACTION FACTOR | 'RF CH4 ' |
| 96 | CH4 (MERGED) RETRIEVAL: PRESSURE (mb) | 'PRCH4M ' |
| 97 | CH4 (MERGED) RETRIEVAL: ALTITUDE (km) | 'ALTCH4M ' |
| 98 | CH4 (MERGED) RETRIEVAL: TEMPERATURE (K) | 'TEMPCH4M ' |
| 99 | CH4 (MERGED) RETRIEVAL: VOLUME MIXING RATIO | 'XMIXCH4M ' |
| 100 | CH4 (MERGED) RETRIEVAL: QUALITY PROFILES | 'QUALCH4M ' |
| 101 | CH4 (MERGED) RETRIEVAL: COLUMN SUM (molec/sq.cm) | 'CH4/MRG CS' |
| 102 | HCL RETRIEVAL: PRESSURE (mb) | 'PRHCL ' |
| 103 | HCL RETRIEVAL: ALTITUDE (km) | 'ALTHCL ' |
| 104 | HCL RETRIEVAL: TEMPERATURE (K) | 'TEMPHCL ' |
| 105 | HCL RETRIEVAL: VOLUME MIXING RATIO | 'XMIXHCL ' |
| 106 | HCL RETRIEVAL: QUALITY PROFILES | 'QUALHCL ' |
| 136 | HCL RETRIEVAL: RETRIEVAL FLAG | 'RFLGHCL ' |
| 107 | HCL RETRIEVAL: AEROSOL TRANSMISSION | 'ATRANHCL ' |
| 108 | HCL RETRIEVAL: AEROSOL EXTINCTION (1/km) | 'AEXHCL ' |
| 109 | HCL RETRIEVAL: COLUMN SUM (molec/sq.cm) | 'HCL CS ' |
| 148 | HCL RETRIEVAL: REFRACTION FACTOR | 'RF HCL ' |
| 110 | HF RETRIEVAL: PRESSURE (mb) | 'PRHF ' |
| 111 | HF RETRIEVAL: ALTITUDE (km) | 'ALTHF ' |
| 112 | HF RETRIEVAL: TEMPERATURE (K) | 'TEMPHF ' |
| 113 | HF RETRIEVAL: VOLUME MIXING RATIO | 'XMIXHF ' |
| 114 | HF RETRIEVAL: QUALITY PROFILES | 'QUALHF ' |
| 137 | HF RETRIEVAL: RETRIEVAL FLAG | 'RFLGHF ' |
| 115 | HF RETRIEVAL: AEROSOL TRANSMISSION | 'ATRANHF ' |
| 116 | HF RETRIEVAL: AEROSOL EXTINCTION (1/km) | 'AEXHF ' |
| 117 | HF RETRIEVAL: COLUMN SUM (molec/sq.cm) | 'HF CS ' |
| 149 | HF RETRIEVAL: REFRACTION FACTOR | 'RF HF ' |
| 118 | INTERFERINGING GAS PROFILE: PRESSURE (mb) | 'IGPR ' |
| 119 | INTERFERINGING GAS PROFILE: ALTITUDE (km) | 'IGALT ' |
| 120 | INTERFERINGING GAS PROFILE: TEMPERATURE (K) | 'IGTEMP ' |
| 121 | INTERFERINGING GAS PROFILE: VOLUME MIXING RATIO (N2O) | 'IGN2O ' |
| 122 | INTERFERINGING GAS PROFILE: QUALITY PROFILES | 'QUALIG ' |
| 123 | INTERFERINGING GAS PROFILE: AEROSOL TRANSMISSION | 'ATRAIG ' |
| 124 | INTERFERINGING GAS PROFILE: AEROSOL EXTINCTION (1/km) | 'AEXIG ' |
| 125 | INTERFERINGING GAS PROFILE: COLUMN SUM (molec/sq.cm) | 'IG CS ' |
| 150 | TEMPERATURE AT 0.3 KM SPACING (K) | 'LV2TEMP ' |
| 151 | PRESSURE AT 0.3 KM SPACING (K) | 'LV2PRES ' |
| 152 | TEMPERATURE USED FOR AEROSOL REMOVAL | 'AEROTEMP ' |
| 153 | PRESSURE USED FOR AEROSOL REMOVAL | 'AEROTEMP ' |
| 154 | ALTITUDE USED FOR AEROSOL REMOVAL | 'AEROTEMP ' |
| 210 | AEROSOL RETRIEVAL: PRESSURE (mb) | 'aero p ' |
| 209 | AEROSOL RETRIEVAL: ALTITUDE (km) | 'aero z ' |
| 211 | AEROSOL RETRIEVAL: TEMPERATURE (K) | 'aero t ' |
| 212 | AEROSOL RETRIEVAL: H2SO4 Percentage by weight | 'aero h2so4' |
| 213 | NO AEROSOL EXTINCTION (1/km) | 'aExHi NO ' |
| 214 | NO AEROSOL EXTINCTION UNCERTIANTIES (1/km) | 'aerStd NO ' |
| 215 | CH4 AEROSOL EXTINCTION (1/km) | 'aExHi CH4 ' |
| 216 | CH4 AEROSOL EXTINCTION UNCERTIANTIES (1/km) | 'aerStd CH4' |
| 217 | HCL AEROSOL EXTINCTION (1/km) | 'aExHi HCl ' |
| 218 | HCL AEROSOL EXTINCTION UNCERTIANTIES (1/km) | 'aerStd HCl' |
| 219 | HF AEROSOL EXTINCTION (1/km) | 'aExHi HF ' |
| 220 | HF AEROSOL EXTINCTION UNCERTIANTIES (1/km) | 'aerStd HF ' |
| 221 | CO2 AEROSOL EXTINCTION (1/km) | 'aExHi CO2 ' |
| 222 | CO2 AEROSOL EXTINCTION UNCERTIANTIES (1/km) | 'aerStd CO2' |
| 228 | Aerosol Density (g/cm^3) | 'AERO_DENSI' |
| 229 | Aerosol Median Radius (micron) | 'MEDIAN_RAD' |
| 230 | Aerosol Distribution Width | 'DIST_WIDTH' |
| 231 | Concentration (/cm^3) | 'CONCENTRAT' |
| 232 | Aerosol Surface Area (micron^2 / cm^3) | 'SFC_AREA ' |
| 233 | Aerosol Volume (micron^3 / cm^3) | 'VOLUME ' |
| 234 | Effective Radius (micron) | 'EFFEC_RAD ' |
| 226 | NO2 Slant Path column amount | 'SLPATH_NO2' |
| 227 | NO Slant Path Column amount | 'SLPATH_NO ' |
| ----------------------------------------------------------------------- |
| NOTES: EACH FILE COVERS ONE DAY OF DATA. THE QUALITY FIELDS ARE IN TERMS OF STANDARD DEVIATIONS AND REPRESENT A PRECISION ESTIMATE OF THE DATA, NOT AN ACCURACY. |