November 1, 2002

DRAFT

This is a work-in-progress document describing the access of level 0, level 1, and level 2 data from the Improved Stratospheric and Mesospheric Sounder (ISAMS) instrument, which is part of a complement of instruments on the Upper Atmosphere Research Satellite (UARS). Primarily, ISAMS measures important minor constituents and temperature in the earth’s stratosphere and mesosphere. Originally, the data were (are) generated for computer systems compatible with the Compaq (Digital Equipment Corporation (DEC)) VAX/Alpha computers running under the VMS operating system. The following describes those data that are converted to be compatible with Silicon Graphics Incorporated (SGI) computer systems running under IRIX, and therefore also with the facilities of the GSFC Distributed Active Archive Center (DAAC). The following also describes software for the access of the converted data files.

Science Systems and Applications Incorporated (SSAI)

Lanham, Md.

1.0 Introduction.	4

1.1 Data Products and File Names.	4

1.1.1 Level 0 Data Products and File Names	4

1.1.2 Level 1 Data Products and File Names	5

1.1.3 Level 2 Data Products and File Names	5

1.2 Software Products and File Names.	6

1.2.1. Level 0 Software	7

1.2.2 Level 1 Software	7

1.2.3 Required Level 2 Software	8

1.3 Additional Software	8

1.3.1 Additional level 0 Software	8

1.3.2 Additional Level 1 software	9

1.3.3 Additional Level 2 software	9

2.0 Related Documentation	10

3.0 ISAMS Files and Data Structure	10

3.1 HRDI Level 0 Files and Data Structures	10

3.2 ISAMS Level 1 File and Data Structures	11

3.3 ISAMS Level 2 File and Data Structures	11

4.0 Access Software	12

4.1 General Considerations.	12

4.1.1 Arrays	12

4.1.2 Fill Data.	12

4.2 Level 0 Fortran Software	13

4.2.1 Fortran Access Routine to Read Level 0 Data (fth_readl0)	13

4.3 Level 0 C Software	14

4.3.1 C Function Routine to Read Level 0 Data (mcb_readl0_c)	14

4.4 Level 1 Fortran Software	15

4.4.1 Level 1 Fortran Access Routine (fth_rwlev1_str)	15

4.4.2 Level 1 C Software	15

4.5 Level 1 C Software	16

4.5.1 Level 1 C Access Code (fth_read_isams_l1_c)	16

4.5.2 Level 1 C Access Array Transform Routines	16

4.6 Level 2 Fortran Software	17

4.6.1 Level 2 Fortran File Header Access Routine (fth_rwl2fh)	17

4.6.2 Level 2 Fortran Mode Header Access Routine (fth_rwl2mh)	18

4.6.3 Level 2 Fortran Data Access Routine (fth_rwl2dr)	18

4.7 Level 2 C Software	19

4.7.1 Level 2 C File Header Access Routine (fth_rwl2fh_c)	19

4.7.2 Level 2 C Mode Header Access Code (fth_rwl2mh_c)	20

4.7.3 Level 2 C Data Record Access Code (fth_rwl2dr_c)	20

Appendix: Additional Software	22

A.1 Additional Level 0 Fortran Software	22

A.1.1 Level 0 Fortran File Open Routine (opn_l0_file)	22

A.1.2 Level 0 Fortran File Name Routine (gen_l0_name)	23

A.1.3 Level 0 Sample Fortran Driver AND Link Procedure	24

A.2 Additional Level 0 C Software.	25

A.2.1 Level 0 C File Open Function Routine (opn_l0_file_c)	25

A.2.2 Level 0 C File Name Function Routine (gen_l0_name_c)	26

A.2.3 Level 0 Sample C Driver and Link Procedure	26

A.3 Additional Level 1 Fortran Software.	27

A.3.1 Level 1 Fortran File Open Routine (opn_l1_file)	27

A.3.2 Level 1 Fortran File Name Routine (gen_l1_name)	29

A.3.3 Level 1 Sample Fortran Driver and Link Procedure	29

A.4 Additional Level 1 C Software.	30

A.4.1 Level 1 C File Open Function (opn_l1_file_c)	30

A.4.2 Level 1 C File Name Function (gen_l1_name_c)	31

A.4.3 Level 1 Sample C Driver and Link Procedure	31

A.5 Additional Level 2 Fortran Software	32

A.5.1 Level 2 Fortran File Open Routine (opn_l2_file)	32

A.5.2 Level 2 Fortran File Name Routine (gen_l2_name)	34

A.5.3 Level 2 Sample Fortran  Driver and Link Procedure	34

A.6 Additional Level 2 C Software	35

A.6.1 Level 2 C File Open Code (opn_l2_file_c)	35

A.6.2 Level 2 C File Name Function (gen_l2_name_c)	36

A.6.3 Level 2 Sample C Driver and Link Procedure	36

# 1.0 Introduction.

This document describes the access of level 0, level 1, and level 2 data from the Improved Stratospheric and Mesospheric Sounder (ISAMS) instrument, which is part of a complement of instruments on the Upper Atmosphere Research Satellite (UARS). Primarily, ISAMS measures temperature and important minor constituents in the earth’s stratosphere and mesosphere. Currently, this document applies to ISAMS level 0, level 1, and level 2 data files that have been converted to be compatible with Silicon Graphics computers running under IRIX. The converted files are also compatible with the facilities of the NASA GSFC Distributed Active Archive Center (DAAC). The original files were created by UARS production processing running under the Compaq (Digital Equipment Corporation (DEC)) VMS operating system, on the UARS Central Data Handling Facility (CDHF). Corresponding activities for the UARS instrument calibration data will be included at a later date. The conversion of UARS level 3 data is not part of this activity.

The software that does the actual conversion of the original files is also not part of this description. The following describes the converted files and the software that are provided to access the converted files. Routines to read the converted file are provided in both Fortran and C. The original data were produced using Fortran code.

## 1.1 Data Products and File Names.

Data products consist of the various levels of ISAMS data. Basically, the level 0 data are the telemetry data that have been sorted. Level 1 data include calibrated data in engineering units, such as radiances, while level 2 data are the products used for scientific analysis, such as temperature and mixing ratios of atmospheric constituents. The data files within a data level are further divided by subtypes, such as the specific parameter(s) measured. As described in more detail below, file names are based on the data level, on the data type (subtype), and on the day of year, among other things. Examples of subtypes are temperature and radiances.

### 1.1.1 Level 0 Data Products and File Names

Nominally, there are 15 types of UARS level 0 files generated for each day. Of these, 5 files are pertinent to ISAMS. Examples are as follows:

isams_l0_d2370.v0002_c01_prod

engineering_l0_d1101.v0002_c01_prod

spacecraft_l0_d2373.v0002_c01_prod

obc_l0_d1673.v0002_c01_prod

quality_l0_d1644.v0002_c01_prod

The UARS level 0 file name convention begins with the type acronym (e.g., isams, engineering,...), followed by the level(i.e., l0). Next is the UARS day number (e.g.,2370; September 12, 1991 corresponds to UARS day number 1, January 19 1992 is UARS day 130). This is followed by the data version number (0002), and then by the cycle number (01). The data version number corresponds to the software that produced the data. For each data version, there is a cycle number that is nominally 1. If reprocessing is needed for the same version, the cycle number is incremented. The most recent data correspond to the highest version and cycle numbers. The last four characters of the file name are always 'prod'.

In the above, file isams_l0_d2370.v0002_c01_prod is the isams level 0 data for UARS day 2370, data version 0002, cycle 01, while the other 4 types of files contain complementary flight data.

### 1.1.2 Level 1 Data Products and File Names

There is one type (subtype) of ISAMS level 1 data files that is converted and archived. Nominally the files are generated on a daily basis and there is one file for each day. A typical file name is

isams_l1_sdata_d0372.v0012_c01_bnbe

The UARS file name convention begins with the instrument acronym (ISAMS), followed by the level (l1), which in turn is followed by the subtype (data). Next is the UARS day number (0372, e.g., September 12, 1991 corresponds to UARS day number 1, and January 1 1992 is UARS day 112) and the data version number (0012), followed by the cycle number (01). The data version is set by the principal investigator, and corresponds to the software version. If reprocessing is needed for the same version, the cycle number is incremented, beginning with 1. The last four characters are 'prod' as originally generated on the UARS CDHF, but have been replaced here by 'bnbe' to denote that they have been converted.

### 1.1.3 Level 2 Data Products and File Names

Several types (subtypes) of ISAMS level 2 data are converted and archived. Examples of file names for the different subtypes for UARS day 120 are

isams_l2_saero10p0_d0120.v0012_c01_prod

isams_l2_saero11p4_d0120.v0012_c01_prod

isams_l2_saero12p1_d0120.v0012_c01_prod

isams_l2_saero16p3_d0120.v0012_c01_prod

isams_l2_saero4p51_d0120.v0012_c01_prod

isams_l2_saero5p28_d0120.v0012_c01_prod

isams_l2_saero6p23_d0120.v0012_c01_prod

isams_l2_saero6p76_d0120.v0012_c01_prod

isams_l2_saero7p43_d0120.v0012_c01_prod

isams_l2_saero7p81_d0120.v0012_c01_prod

isams_l2_saero8p09_d0120.v0012_c01_prod

isams_l2_sch4_d0120.v0012_c01_prod

isams_l2_sco_d0120.v0012_c01_prod

isams_l2_sh2o_d0120.v0012_c01_prod

isams_l2_shno3_d0120.v0012_c01_prod

isams_l2_sn2o_d0120.v0012_c01_prod

isams_l2_sn2o5_d0120.v0012_c01_prod

isams_l2_sno_d0120.v0012_c01_prod

isams_l2_sno2_d0120.v0012_c01_prod

isams_l2_so3_d0120.v0012_c01_prod

isams_l2_spres_d0120.v0012_c01_prod

isams_l2_stemp_d0120.v0012_c01_prod

isams_l2_s00prad_d0120.v0012_c01_prod

isams_l2_s00wrad_d0120.v0012_c01_prod

isams_l2_s10prad_d0120.v0012_c01_prod

isams_l2_s10wrad_d0120.v0012_c01_prod

isams_l2_s10x_d0120.v0012_c01_prod

isams_l2_s11a_d0120.v0012_c01_prod

isams_l2_s11x_d0120.v0012_c01_prod

isams_l2_s121x_d0120.v0012_c01_prod

isams_l2_s16x_d0120.v0012_c01_prod

isams_l2_s20prad_d0120.v0012_c01_prod

isams_l2_s20wrad_d0120.v0012_c01_prod

isams_l2_s30prad_d0120.v0006_c01_prod

isams_l2_s30wrad_d0120.v0006_c01_prod

isams_l2_s31prad_d0120.v0006_c01_prod

isams_l2_s31wrad_d0120.v0006_c01_prod

isams_l2_s32wrad_d0120.v0012_c01_prod

isams_l2_s33wrad_d0120.v0012_c01_prod

isams_l2_s40prad_d0120.v0012_c01_prod

isams_l2_s40wrad_d0120.v0012_c01_prod

isams_l2_s45x_d0120.v0012_c01_prod

isams_l2_s50prad_d0120.v0012_c01_prod

isams_l2_s50wrad_d0120.v0012_c01_prod

isams_l2_s53a_d0120.v0012_c01_prod

isams_l2_s53x_d0120.v0012_c01_prod

isams_l2_s60prad_d0120.v0012_c01_prod

isams_l2_s60wrad_d0120.v0012_c01_prod

isams_l2_s62x_d0120.v0012_c01_prod

isams_l2_s68x_d0120.v0012_c01_prod

isams_l2_s70prad_d0120.v0006_c01_prod

isams_l2_s70wrad_d0120.v0006_c01_prod

isams_l2_s71prad_d0120.v0006_c01_prod

isams_l2_s71wrad_d0120.v0012_c01_prod

isams_l2_s72wrad_d0120.v0012_c01_prod

isams_l2_s73wrad_d0120.v0012_c01_prod

isams_l2_s74x_d0120.v0012_c01_prod

isams_l2_s78x_d0120.v0012_c01_prod

isams_l2_s81x_d0120.v0012_c01_prod

The file name convention is the same as that for level 1 files, as described above.

## 1.2 Software Products and File Names.

The software products are divided into required software and additional products. The required software consists of access functions/routines in both Fortran and C that can be used to read the files. Additional software are those which are provided as a convenience for the user and is not formally part of this software package. Examples of additional software are sample drivers that use the required software, and routines that generate the proper file names and open the files. Additional software are described in the Appendix.

Because some of the software is made to run under both IRIX and under VMS, for the sake of consistency, the following file name conventions are used for the software. Files names for Fortran code end in '.for', and files written in C will end in '.c'. Link scripts and executable names end in '.com' and '.exe', respectively.

The names of the software modules are listed next. The software are given in terms of subroutine/function names or file names. The subroutine/function names and file names are used interchangeably, but the latter also contain extensions such as '.for', as noted above.

### 1.2.1. Level 0 Software

The following routine/function can be used to read each of the 5 level 0 files listed above. File names are given in parenthesis.

Routine name                 Description

(file name)

------------                 -----------

fth_readl0                   Fortran routine to read level 0 files of

(fth_readl0.for)             all types

mcb_readl0_c                 C code to read level 0 files of all types

(mcb_readlo_c.c)

### 1.2.2 Level 1 Software

Software is provided to read header and data records for each of the files listed above.

Routine name                 Description

(file name)

fth_rwlev1_str               Fortran routine to read both header and

(fth_rwlev1_str.for)         data records of the ISAMS level 1 file

(subtype DATA)

fth_read_isams_l1_c          C code to read both header and

(fth_read_isams_l1_c.c)      data records of the ISAMS level 1 file

(subtype DATA).

The following C code is also provided to transform multidimensional arrays such that C and Fortran software present the arrays in the same manner (consistent with Fortran). However, users need not be concerned with their usage, as they are used only by the read software provided. Users need only link the following C files:

for_c_mtrx_4 (for_c_mtrx_4.c)

int_for_c_mtrx_2 (int_for_c_mtrx_2.c)

int2_for_c_mtrx_4 (int2_for_c_mtrx_4.c)

int_for_c_mtrx_3 (int_for_c_mtrx_3.c)

int2_for_c_mtrx_2 (int2_for_c_mtrx_2.c)

int2_for_c_mtrx_3 (int2_for_c_mtrx_3.c)

ch_for_c_mtrx_2 (ch_for_c_mtrx_2.c)

ch_for_c_mtrx_3 (ch_for_c_mtrx_3.c)

test_nan_c (test_nan_c.c)

### 1.2.3 Required Level 2 Software

Module name                 Description

(file name)

-----------                 -----------

fth_rwl2fh                  Fortran routine to read ISAMS level 2

(fth_rwl2fh.for)            file header records

fth_rwl2mh                  Fortran routine to read ISAMS level 2

(fth_rwl2mh.for)            mode header records

fth_rwl2dr                  Fortran routine to read ISAMS level 2

(fth_rwl2dr.for)            file data records

fth_rwl2fh_c                C code to read ISAMS level 2

(fth_rwl2fh_c.c)            file header records

fth_rwl2mh_c                C code to read ISAMS level 2

(fth_rwl2mh_c.c)            mode header records

fth_rwl2dr_c                Fortran routine to read ISAMS level 2

(fth_rwl2dr_c.c)            file data records

## 1.3 Additional Software

As noted earlier, additional software is provided as a convenience to users, but is not formally part of the software package per se. Used together with the access routines, they can be linked into executables to read and list the data. Here, they are listed for completeness. Details are given in the Appendix. File names are given in parenthesis.

### 1.3.1 Additional level 0 Software

Routine Name                 Description

(file name)

-----------                  -----------

get_l0                       Fortran sample driver for using level 0

(get_l0.for)                 routines

opn_l0_file                  Fortran code to open level 0 files

(opn_l0_file.for)

gen_l0_name                  Fortran code to generate level 0 file names

(gen_l0_name.for)

get_l0_c                     C sample driver for using level 0

(get_l0_c.c)                 function routines

opn_l0_file_c                C code to open level 0 files

(opn_l0_file_c.c)

gen_l0_name_c                C code to generate level 0 file names

(gen_l0_name_c.c)

### 1.3.2 Additional Level 1 software

Name                         Description

(file name)

get_isams_l1_data_str        sample Fortran driver to call routines

(get_isams_l1_data_str.for)  and read level 1 files of subtype DATA

opn_l1_file                  Fortran routine to open level 1 files

(opn_l1_file.for)

gen_l1_name                  Fortran routine to generate level 1

(gen_l1_name.for)            file names for a specific day and data

version

get_isams_l1_data_str_c      sample c code driver to use software to

(get_isams_l1_data_str_c.c)  read level 1 files of subtype DATA

opn_l1_file_c                c code to open level 1 file

(opn_l1_file_c.c)

gen_l1_name_c                c code to generate level 1 file names

(gen_l1_name_c.c)

### 1.3.3 Additional Level 2 software

Module name                  Description

(file name)

get_isams_l2_all_str         sample Fortran driver which uses the

(get_isams_l2_all_str.for)   level 2 access routines(all subtypes)

opn_l2_file                  Fortran routine to open level 2 files

(opn_l2_file.for)

gen_l2_name                  Fortran routine to generate level 2 file

(gen_l2_name.for)            names

get_isams_l2_all_str_c       sample c code driver which uses level 2a

(get_isams_l2_all_str_c.c)   access software(all subtypes)

opn_l2_file_c                c code to open level 2a and 2b files

(opn_l2_file_c.c)

gen_l2_name_c                c code to generate level 2 file names

(gen_l2_name_c.c)

# 2.0 Related Documentation

A general description of the scientific goals and of the instrument is found in the following journal paper:

Taylor, F. W., C. D. Rodgers, J. G. Whitney, S. T. Werret, J. J. Barnett, G. D. Peskett, P. Venters, J. Ballard, C. W. P. Palmer, R. J. Knight, P. Morris, T. Nightingale, and A. Dudhia, Remote sensing of Atmospheric Structure and Composition by Pressure Modulator Radiometry From Space:The ISAMS Experiment on UARS, J. Geophys. Res., 98, 10,799-10,814, June 20, 1993.

Other related ISAMS documents are

a) UPPER ATMOSPHERE RESEARCH SATELLITE IMPROVED STRATOSPHERIC AND

MESOSPHERIC SOUNDER EXPERIMENT DATA PROCESSING SOFTWARE USERS' GUIDE,

13th April, 1995

This document is contained in file NURSIS01.DOC.

b) ISAMS LEVEL2 DATA STRUCTURE in UARS STANDARD DOCUMENTATION FORMAT

This document is contained in file USER_GUIDE_ISM.TXT.

c) UARS CDHF SOFTWARE SYSTEM (UCSS) PROGRAMMER'S GUIDE TO PRODUCTION

SOFTWARE SUPPORT SERVICES, COMPUTER SCIENCES CORPORATION, FEBRUARY,

1993.

This document describes access routines for UARS data levels 0 and 3, but not for levels 1 and 2. However, there is still general information that may be useful to users. This document can be obtained from the UARS Program Assistance Center (PAC).

Currently, there is no documentation available per se for the level 1 data.

# 3.0 ISAMS Files and Data Structure

## 3.1 HRDI Level 0 Files and Data Structures

Unlike the converted level 1 and level 2 files, the level 0 files are unchanged from their original VMS versions. The contents of level 0 files are mostly byte-oriented, and the relatively few data words  need to be converted are done so by the read routine that is provided and described below. Consequently, users should only use the included software for this purpose.

All Level 0 files contain fixed length records, and data access is direct. The record lengths for relevant file types are as follows

TYPE         RECORD LENGTH (BYTES)

----         ---------------------

isams         8256

engineering   8256

spacecraft   21568

obc          14400

quality       2532

For more details, refer to the document

UARS CDHF SOFTWARE SYSTEM (UCSS) PROGRAMMER'S GUIDE TO PRODUCTION

SOFTWARE SUPPORT SERVICES, COMPUTER SCIENCES CORPORATION,OCTOBER,1995.

The contents can be found in file

UCSS_PG_OCT95.MEM

## 3.2 ISAMS Level 1 File and Data Structures

As noted above, an example of a converted level 1 ISAMS file is

isams_l1_sdata_d0372.v0012_c01_bnbe

The data files of subtype DATA are the primary Level 1 products. There are also level files with subtype LOG, which are production processing LOG files and are not converted for archival purposes.

The level 1 files (subtype DATA) consist of fixed length records written in binary. All files have the same record length, namely, 3840 words (four bytes). Data in the converted files appear in the same order and the same records as in the original VMS files, and direct access in reading the records can be used.

Currently, there is no available documentation per se on the level 1 data.

## 3.3 ISAMS Level 2 File and Data Structures

Examples of converted level 2 files are

isams_l2_so3_d0120.v0012_c01_bnbe

isams_l2_stemp_d0120.v0012_c01_bnbe

The level 2 files (various subtypes) consist of fixed length records, but the record lengths may be different for different files, even for the same subtype (e.g., temperature). With the exception of the first record (Standard Formatted Data Unit (SFDU), which is related to metadata data), data in the converted files appear in the same order and the same records as in the original VMS files. The exception is that the value of the record length of the file has been added as an additional (last) word of the first record. In the original files, the value of the record length is part of the second record (and remains there as well in the converted files). Although the original files are fine for VMS Fortran, this is problematical for reading under UNIX. Therefore the addition of the record length value to record 1. Direct access can be used.

Documentation titled ‘ISAMS LEVEL2 DATA STRUCTURE in UARS STANDARD DOCUMENTATION FORMAT’ is contained in the file USER_GUIDE_ISM.TXT.

# 4.0 Access Software

Software for accessing the data is provided in the form of Fortran routines and C functions. For consistency, because software is provided in both Fortran and C, and because some of the software are made to run under both IRIX and under VMS, the following name conventions are used for the software: a) file names for Fortran code end in '.for', and files written in C end in '.c'; b) link scripts and executable file names end in '.com' and '.exe', respectively.

For Fortran, the code was culled and adapted from the ISAMS production software. Efforts have been made to keep a reasonable semblance to the original code. For example, in the original routine for the mode header (RWL2MH) access, after reading the records, the first 3 elements of buffer L2MHRB are changed. The current access routines for Fortran keeps this code. For C, the routine merely reads the data records and make no further changes.

## 4.1 General Considerations.

The ISAMS level 1 and level 2 data files were originally written in binary with fixed record lengths, and the converted files contain the same records and structures. Record data access is direct.

Because the structure of the records has been preserved, the original ISAMS documentation remain applicable, but with the following  issues in this section borne in mind.

### 4.1.1 Arrays

The indices of arrays that are read by Fortran routines begin with the same values as in the original VMS routines. Arrays that are read by C programs begin with index 0.

For multidimensional arrays, C and Fortran are different as to which index varies fastest (row major, row minor). The C access routines which are provided accounts for this, so that the various indices of the arrays have the same meaning for both C and Fortran routines, and conform to the original documentation.

### 4.1.2 Fill Data.

The original VMS files use an 'illegal floating point' number for fill data. This number in HEX is '8000'X. In agreement with ISAMS, it is thought that this is inconvenient, especially for unsuspecting users. Therefore, the converted files use the value -999.9E+30 for fill data.

## 4.2 Level 0 Fortran Software

### 4.2.1 Fortran Access Routine to Read Level 0 Data (fth_readl0)

Because the level 0 data files are unchanged from the original VMS versions, users should use only fth_readl0 (file fth_readl0.for), or its C equivalent, for reading the level 0 data on systems which conform to the big endian addressing convention (e.g., SGI, SUN). The level 0 data files are essentially byte-oriented, and only the first 64 bytes of the data records (the data record header) need be converted. It was judged that this conversion should be done by the read routine. Record access is direct, and record 1 is the file label record (all ASCII) followed by data records. The first 64 bytes of each data record (the data record header) are mostly information in integer words, and is converted by the read software. The rest of each data record is byte-oriented.

Usage:

CALL FTH_READL0(LUN_RD,IREC,IREC_LEN,L0_BUFF,

& ISWAP,IOS_RD)

ARGUMENT DESCRIPTION

ARGUMENT      TYPE        I/O     DESCRIPTION

--------      ----        ---     -----------------------------

LUN_RD        I*4         I       LOGICAL UNIT OF INPUT FILE

IREC          I*4         I       RECORD TO READ (1 OR GREATER)

IREC_LEN      I*4         I       RECORD LENGTH IN BYTES

claes        24640

haloe        16448

hrdi         19520

isams         8256

mls          10304

pem          28736

solstice      2532

susima        8256

susimb        8256

windii       16448

acrim         4160

engineering   8256

spacecraft   21568

obc          14400

quality       2532

L0_BUFF       CHAR*1      O       BUFFER CONTAINING LEVEL 0 DATA

(IREC_LEN)

ISWAP         I*4         I       0:FOR LITTLE ENDIAN COMPUTERS

1:FOR BIG ENDIAN COMPUTERS

IOS_RD        I*4         O       READ STATUS 0:NO ERROR

This routine calls 3 other routines that are used to convert from little endian to big endian standards, namely,

swap32 (swap32.for)

swap16 (swap16.for)

swap64 (swap64.for)

The file names are in parenthesis). Users need not know how to call these routines explicitly as they are used only by fth_readl0.

## 4.3 Level 0 C Software

### 4.3.1 C Function Routine to Read Level 0 Data (mcb_readl0_c)

Because the level 0 data files are unchanged from the original VMS versions, users should use only mcb_readl0_c (file mcb_readl0_c.c), or its Fortran equivalent, for reading the level 0 data on systems which conform to the big endian addressing convention (e.g., SGI, SUN).

Usage:

void mcb_readl0_c(FILE *fp_rd,int irec,int in_recl_byte,

signed char *l0_buff,int iswap,int *ios_rd);

mcb_readl0_c(fp_rd,irec,in_recl_byte,&l0_buff[0],iswap,&ios_rd);

-----------------------------------------------------------------------

THIS ROUTINE READS THE UARS LEVEL 0 DATA. IT ASSUMES

THAT THE DATA FILE CORRESPONDS TO THE ORIGINAL, VMS

DATA FILES. IN ORDER TO INTERPRET CORRECTLY, FOR

BIG ENDIAN COMPUTERS, ISWAP SHOULD BE SET TO 1.

-----------------------------------------------------------------------

ARGUMENT DESCRIPTION

ARGUMENT      TYPE        I/O     DESCRIPTION

--------      ----        ---     -----------------------------

fp_rd         FILE*       I       pointer to input file-buffer-string

irec          I*4         I       RECORD NUMBER TO READ (1 OR GREATER)

irec_len      I*4         I       RECORD LENGTH IN BYTES

l0_buff       CHAR*1      O       BUFFER CONTAINING LEVEL 0 DATA

iswap         I*4         I       0:FOR LITTLE ENDIAN COMPUTERS

1:FOR BIG ENDIAN COMPUTERS

ios_rd        I*4         O       READ STATUS 0:NO ERROR

-----------------------------------------------------------------------

This routine calls 3 other routines that are used to convert from

little endian to big endian standards, namely,

swap32_c (swap32_c.c)

swap16_c (swap16_c.c)

swap64_c (swap64_c.c)

Users need not know how to invoke these routines explicitly as they are used only by mcb_readl0_c.

## 4.4 Level 1 Fortran Software

The required software consists of one routine that users can call to read the level 1 header and data records. Additional software in the form of a sample driver, a file name generation routine, and a file open routine is provided.  A procedure is also provided to link the driver and routines.  The resulting executable can be used to read the data and write selected portions to an output file for analysis. More details are given in the Appendix.

### 4.4.1 Level 1 Fortran Access Routine (fth_rwlev1_str)

Routine fth_rwlev1_str (file fth_rwlev1_str.for) reads both the header and data records of the ISAMS level 1 data (subtype DATA). Aside from opening the data file, it is the only routine necessary. It is called with similar arguments as the original ISAMS routine named RWLEV1. The exception is the argument for read/write has been removed, so that only reads are implemented.

Usage:

CALL FTH_RWLEV1_STR(LUN1,EMFCNT,DHFLAG,FAIL,ERRMSG,IOS)

Argument description.

NAME       TYPE          I/O     DESCRIPTION

----       ----          ---     ----------------------------------

LUN1       I*4           I       Logical Unit Number of level 1

data file.

EMFCNT     I*4           I       The number of the EMAF being read.

DHFLAG     CHAR          I       'H' for header, 'D' for data to

read.

FAIL       LOGICAL       O       True if error occurs, otherwise

false.

ERRMSG     CHAR*80       O       If error occurs, reports what went

wrong.

IOS        I*4           O       Fortran read status return code

The data values are available to the calling routine in common blocks.  At this time, there is no separate documentation for the description of the variables, except for that in the in-line comments of the code.  Users should review the sample driver described below for in-line comments.

### 4.4.2 Level 1 C Software

As in the Fortran case, the required software consists of one routine which users can call to read both the level 1 header and data records. Additional software in the form of a sample driver, a file name generation routine, and a file open routine are provided.  A procedure is also provided to link the driver and routines.  The resulting executable can be used to read the data and write selected portions to an output file for analysis.

## 4.5 Level 1 C Software

### 4.5.1 Level 1 C Access Code (fth_read_isams_l1_c)

C function fth_read_isams_l1_c (file fth_read_isams_l1_c.c) reads the ISAMS level 1 data (subtype DATA), both header and data records.

Usage:

void fth_read_isams_l1_c(FILE* ifp,int* rlen,int itype,int irec_rd,

struct l1hdr *l1hdr_rec, struct l1dtr *l1dtr_rec, int

ifile_type,int* ios)

Argument list description:

NAME      TYPE      I/O    DESCRIPTION

----      -------   ---    ----------------------------------------

ifp       FILE      I      FILE pointer associated with opened

POINTER          file.

rlen      int       I      length of file records.

itype     int       I      1:read header record. 2:read data

record.

irec_rd   int       I      record number to read

l1hdr_rec structure O      header data read. corresponds to, and

organized like Fortran COMMON l1hdr in

original ISAMS Fortran code.

See include file LV1COM.I

l1dtr_rec structure O      data record read. corresponds to, and

organized like Fortran COMMON l1dtr in

original ISAMS Fortran code.

See include file LV1COM.I

ifile_type int      I      not used for now.

ios        int      O      read error code. 0:no error.

As noted for the corresponding Fortran access routine, there is currently no independent documentation available which describe the variables other than the in-line comments of the original ISAMS Fortran code.

### 4.5.2 Level 1 C Access Array Transform Routines

Because C and Fortran storage for multidimensional arrays are not consistent with each other (row major, row minor), software is needed to transform the multidimensional arrays after reading from disk, so that they are interpreted in the same manner by both C and Fortran.  These are as follows (file names are in parenthesis):

for_c_mtrx_4 (for_c_mtrx_4.c)

int_for_c_mtrx_2 (int_for_c_mtrx_2.c)

int2_for_c_mtrx_4 (int2_for_c_mtrx_4.c)

int_for_c_mtrx_3 (int_for_c_mtrx_3.c)

int2_for_c_mtrx_2 (int2_for_c_mtrx_2.c)

int2_for_c_mtrx_3 (int2_for_c_mtrx_3.c)

ch_for_c_mtrx_2 (ch_for_c_mtrx_2.c)

ch_for_c_mtrx_3 (ch_for_c_mtrx_3.c)

test_nan_c (test_nan_c.c)

Users do not need to know how to use these routines, as they are called only by the function routine fth_read_isams_l1. Using the link procedure file given in the Appendix will automatically link these routines.

## 4.6 Level 2 Fortran Software

The required software consists of 3 routines that are based on the original ISAMS production processing software. The first routine reads the SFDU and file header records (numbers 1 and 2). The second routine reads the mode header records a and b, and the third reads the data records. The routines should be used in the order given here because information from the header records is needed for reading the data records. As noted earlier, additional software which use these routines, which generate file names, and which open the files are provided as a convenience, and are described in the Appendix.

Level 2 UARS data conform to the Standard Formatted Data Units (SFDU) convention. The SFDU provides information on the origin of the data, and points to additional information about the data. This is contained in the first record(s) of the file.

### 4.6.1 Level 2 Fortran File Header Access Routine (fth_rwl2fh)

Routine fth_rwl2fh (file fth_rwl2fh.for) reads the ISAMS level 2 SFDU record (record 1) and the header record (record 2). Modifications from the original were needed due to the reading of, and adding the record length to the SFDU record (as described above).

Usage:

CALL FTH_RWL2FH(LUNLV2, RLEN, L2FLHD, FAIL, ERRMSG,

&  TZFLD,LZFLD,TIFLD,LIFLD,IRD_MODE,IOS_SFDU)

Argument list description:

NAME       TYPE         I/O   DESCRIPTION

----       ----         ---   -------------------------------------

LUNLV2     I*4          I     Logical Unit Number of level 1 data

file.

RLEN       I*4          O     Length of record in bytes

L2FLHD     BYTE(27)     O     array to hold record header.

FAIL       LOGICAL      O     True if error occurs, otherwise

false.

ERRMSG     CHAR*80      O     If error occurs, reports what went

wrong.

TZFLD      CH*12        O     holds the SFDU information

LZFLD      CH*8         O     holds the SFDU information

TIFLD      CH*12        O     holds the SFDU information

LIFLD      CH*8         O     holds the SFDU information

IRD_MODE   I*4          I     -999: do not read value of record

length

-1: read value of record length from

record

1 and return.

+1: read value of record length and

also

header record (record 2).

IOS_SFDU  I*4           O     error code for SFDU record (number 1)

### 4.6.2 Level 2 Fortran Mode Header Access Routine (fth_rwl2mh)

Routine fth_rwl2mh (file fth_rw_l2mh.for) reads the mode header records.

This software was adapted from the ISAMS routine RWL2MH. The code is the same as the original except that the RW (read/write argument has been removed), and only read capability is implemented.

Usage:

CALL FTH_RWL2MH ( LUNLV2, RLEN, L2MHRA, L2MHRB, MODE,

&                    FAIL, ERRMSG )

Argument list description:

NAME       TYPE           I/O        DESCRIPTION

----       ----           ---        ------------------------------

LUNLV2     I*4            I          Logical Unit Number of level 1

data file.

RLEN       I*4            O          Length of record in BYTES

L2MHRA     BYTE(136)      O          buffer for Header Record A.

See L2SIZE.INC

L2MHRB     BYTE(*)        O          buffer for Header Record B.

See L2SIZE.INC

MODE       I*4            I          Mode Header#

FAIL       LOGICAL        O          set TRUE if an error is

detected

ERRMSG     CH*80          O          error message if failure has

occurred

### 4.6.3 Level 2 Fortran Data Access Routine (fth_rwl2dr)

Routine fth_rwl2dr (file_fthrwl2dr.for) reads the ISAMS level 2 data records. The code  was adapted from the ISAMS routine RWL2DR, and is the same as the original except that RW, the read/write argument has been removed, and only read capability is implemented.

Usage:

CALL FTH_RWL2DR ( LUNLV2, NMODES, NSURF, RLEN, L2DTRC,

&                    PROFIL, FAIL, ERRMSG )

Argument list description:

NAME       TYPE      I/O     DESCRIPTION

----       ----      ---     --------------------------------------

LUNLV2     I*4       I       Logical Unit Number of level 1 data

file.

NMODES     I*4       I       No. of modes in file

NSURF      I*2       I       No. of levels in profile

RLEN       I*4       I       size of Level 2 File Record

L2DTRC     BYTE(*)   O       buffer for Read. See L2SIZE.INC

PROFIL     I*4       I       Data Record# (i.e. Profile#)

FAIL       LOGICAL   O       set TRUE if an error is detected

ERRMSG     CH*80     O       error message if failure has occurred

## 4.7 Level 2 C Software

As in the Fortran case, the required software consists of 3 routines which users can call to read the level 2 files. Also, additional software in the form of a sample driver, a file name generation routine, and a file open routine is provided. A procedure is also provided to link the driver and routines. The resulting executable can be used to read the data and write selected portions to an output file. These are provide as a convenience and described in the Appendix.

### 4.7.1 Level 2 C File Header Access Routine (fth_rwl2fh_c)

Function frh_rwl2fh_c (file fth_rwl2fh_c.c) reads the ISAMS level 2 SFDU and header record.

Usage:

fth_rwl2fh_c(ifp,&rlen_bytes,tzfld,lzfld,tifld,lifld,

&str_l2flhd_rec,ifile_type,&ios);

Argument list description:

NAME             TYPE      I/O   DESCRIPTION

----             ----      ---   ----------------------------------

ifp              FILE      I     FILE pointer associated with

POINTER   I     opened file.

rlen_bytes       int       O     record length in bytes

tzfld            ch*12     O     holds the SFDU information

lzfld            ch*8      O     holds the SFDUinformation

tifld            ch*12     O     holds the SFDU information

lifld            ch*8      O     holds the SFDUinformation

str_l2flhd_rec   structure O     See include file #include l2flhd.i

ifile_type       int       I     2:big endian (should be used

normally)

3:little endian

used to determine file name.

ios              int       O     i/o read error code. 0:no error.

### 4.7.2 Level 2 C Mode Header Access Code (fth_rwl2mh_c)

Function fth_rwl2mh_c (file fth_rwl2mh_c.c) reads ISAMS level 2 mode header records.

Usage:

fth_rwl2mh_c(ifp,&rlen_bytes,irec_rd,&l2mhra_rec,&l2mhrb_rec,

surfs, &contam[0][0],&ios);

Argument list description:

NAME       TYPE     I/O      DESCRIPTION

------       ----     ---      --------------------------------------

ifp        FILE     I        FILE pointer associated with opened

POINTER           file.

rlen_bytes int      I        record length in bytes.

irec_rd    int      I        used for determining record to read

in cases of mode_header_records.

should begin with 1 and end with

nmodes,

where nmodes is obtained from a

previous

read of the file header record.

l2mhra_rec structure O       contains mode header file a

information.

See include file l2mdhd.i

l2mhrb_rec structure O       contains mode header file b

information.

See include file l2mdhd.i

surfs      short int O       NSURF level values [UARS press.*100]

[maxsfc]          or [mirror steps] relative to SFCOFF

in L2DTRC

contam     char      O       list of NCNTAM input contaminant gases

[maxctm][5]         used

and source of data (info from Driver

file)

maxctm = 8. see include file l2size.i

ios        int       O     i/o read error code. 0:no error.

### 4.7.3 Level 2 C Data Record Access Code (fth_rwl2dr_c)

Function fth_rwl2dr_c (file fth_rwl2dr_c.c) reads the ISAMS level 2 data record.

Usage:

fth_rwl2dr_c(ifp,&rlen_bytes,nmodes_ns,nsurf_ns,profil,

&l2dtrc_rec, &ios);

Argument list description:

NAME       TYPE      I/O      DESCRIPTION

----       ----      ---      -------------------------------------

ifp        FILE      I        FILE pointer associated with opened

POINTER            file.

rlen_bytes int       I        record length in bytes.

nmodes_ns  int       I        number of modes and mode header recs

in file.

obtained from header record.

nsurf_ns   int       I        number of profile levels (up to

NSURFM)

obtained from mode_header_record_b.

profil     int       I        data record number to be read

min is 1. max is

str_l2flhd_rec.nprofs;

l2dtrc_rec structure O        contains data record information.

See include file l2dtrc.i

dat2       float     O        radiance/retrieval profile in order

[maxsfc]           given in hdr.

maxsfc = 300. see include file

l2size.i

qual       float     O        rms accuracy of dat2

[maxsfc]

ios        int       O        i/o read error code. 0:no error.

# Appendix: Additional Software

Sample software that uses the file access software described above is described in this Appendix. It should be noted that the software described here is not a formal part of the required software package, and is provided only as a convenience to users. The software described below consists of sample drivers, and functions and routines that generate file names and open the files. These are provided in Fortran and C.

This software, combined with the access software described earlier in the main text, is self-contained, and can be linked into executables. Link procedures are provided and described below.

## A.1 Additional Level 0 Fortran Software

### A.1.1 Level 0 Fortran File Open Routine (opn_l0_file)

The Fortran routine opn_l0_file (file opn_l0_file.for) opens a UARS level 0 file with the proper attributes. It calls routine gen_l0_name (file gen_l0_name.for) to generate the needed filenames based on user-input values such as the instrument acronym, the subtype, the uars day, and the data version, as described above. For each data version, there is a cycle number that is greater than or equal to 1. Users need not know the cycle number as long as the variable ICYC_MAX is set to be larger than the actual cycle number of the file. A value of 10 for ICYC_MAX is usually large enough. Routine opn_l0_file will begin with cycle number 1 and will increment cycle numbers until a file is successfully opened or until ICYC_MAX is reached. The data version number and the cycle number are determined by production processing. The data version number corresponds to the software version that was used to generate the file, and the cycle number is incremented each time reprocessing was needed for the same file using the same software.

Usage:

CALL OPN_L0_FILE(INSTR,IUARS_DAY,IVER_IN,

& ICYC_MAX,ITYPE,IN_RECL,ICYC,LUN,FLNAME,IVAR,IDIRECT,IOS)

ARGUMENT LIST DESCRIPTION

ARGUMENT      TYPE     I/0      DESCRIPTION

--------      ----     ---      -------------------------------------

INSTR         CH*12    I        INSTRUMENT ACRONYM. e.g.,

claes, haloe, hrdi, isams, mls, pem,

solstice, susima, susimb, windii,

acrim,

engineering, spacecraft, obc, quality

IUARS_DAY     I*4      I        UARS DAY.

IVER_IN       I*4      I        DATA VERSION.

ICYC_MAX      I*4      I        MAXIMUM CYCLE NUMBER TO TRY.

ITYPE         I*4      I        SET LAST 4 CHARACTERS OF INPUT FILE

NAME. 1: PROD

2: BNBE

3: BNLE

-2: BVBE

-3: BVLE

IN_RECL       I*4      I        RECORD LENGTH (WORDS) OF

FILE IF FIXED LENGTH.

IF VALUE IS GT 0 FILE IS OPENED

AS WITH RECL KEYWORD SET TO VALUE OF

IN_RECL.

ICYC          I*4      I/O      IF 0 ON INPUT, ROUTINE WILL

TRY TO OPEN EXISTING FILE. CYCLES

NUMBERS FROM 1 TO ICYC_MAX WIIL BE

TRIED. IF EXISTING FILE IS FOUND,

ICYC IS RETURNED. IF FILE NOT FOUND,

ICYC IS SET BACK TO 0.

LUN           I*4      I/O      LOGICAL UNIT NUMBER OF FILE.

IF NOT ZERO ON INPUT, THE INPUT VALUE

IS USED TO OPEN THE FILE.

IF ZERO ON INPUT, LUN WILL

BE SET TO 95 (INPUT) IF ICYC IS 0,

AND TO 96 (OUTPUT) IF ICYC IS NOT 0.

FLNAME        CH*50    O        FLNAME OF FILE.

IVAR          I*4      I        IF O, OPEN FOR FIXED RECORD LENGTH

IF -1, OPEN WITH KEYWORD RECORDTYPE

SET TO 'SEGMENTED'

IF -2, OPEN WITH KEYWORD RECORDTYPE

SET TO 'VARIABLE'

IDIRECT       I*4      I        INPUT 0:SEQUENTIAL ACCESS,1:DIRECT

IOS           I*4      O        STATUS.

### A.1.2 Level 0 Fortran File Name Routine (gen_l0_name)

Routine gen_l0_name (file gen_l0_name.for) generates the correct file name based on user-input values of the instrument and subtype acronyms, the UARS day number, and the file data version.

This routine is called only by opn_l0_file, and users only need to link this routine.

Usage:

CALL GEN_L0_NAME(INSTR,IUARS_DAY,FNAME,IVER,ICYC,

& ITYPE)

ARGUMENT DESCRIPTION:

ARGUMENT      TYPE     I/0      DESCRIPTION

--------      ----     ---      ---------------------------------------

INSTR         CH*12    I        INSTRUMENT ACRONYM.

IUARS_DAY     I*4      I        UARS DAY.

IVER          I*4      I        DATA VERSION.

ICYC          I*4      I        DATA VERSION.

FNAME         CH*50    O        filename

### A.1.3 Level 0 Sample Fortran Driver AND Link Procedure

An example of a driver that uses fth_readl0.for to read all types of level 0 files is provided and given in file

get_l0.for.

The command/script file

get_l0.com

can be used to link and generate an executable named

get_l0.exe

For linking, in addition to the sample driver (get_l0.for), the routines fth_readl0.for, opn_l0_file_unix.for, gen_l0_name.for, swap16.for, swap32.for, and swap64.for (noted earlier) are needed as well.

Upon running program get_l0.exe interactively, the following prompt appears on the screen:

ENTER FILE TYPE NUMBER

1:CLAES,2:HALOE,3:HRDI,4:ISAMS,5:MLS,6:PEM

7:SOLSTICE,8:SUSIMA,9:SUSIMB,10:WINDII,11:ACRIM

12:ENGINEERING,13:SPACECRAFT,14:OBC,15:QUALITY

ENTER UARS DAY

ENTER FIRST DATA RECORD NUMBER, LAST DATA RECORD NUMBER'

(-1 FOR BOTH TO DO ALL DATA RECORDS)

DATA VERSION NUMBER,WRITE ASCI FILE[0/1]

SWAP BYTES[0/1]

An example of a user input to this prompt is

12 130 1 10 2 1 1

The different input variables are separated with blanks. As described in the prompt, the first input, ‘12’, selects the ENGINEERING file to open and read. The 130 selects the UARS day to read (there is one file for each day). Recall that UARS day number 1 is September 12, 1991, and January 1 1992 corresponds to UARS day 112. The '1 10' selects the first and last data records wanted (in this case the first 10 records). The next input, '2', is the file data version number. The next to last input, ‘1’, means that an output file of selected data will be written. The last input, also ‘1’, is used for big endian computers, and a value of ‘0’ is input for little endian systems.

With the above input, the program will read the first 10 data records of the level 0 data file named

engineering_l0_d0130.v0002_c01_prod

and write a text file  named

engineering_l0_d0130.v0002_c01_asci

containing certain portions of data from the 10 selected records.

UARS file name conventions have been described in Section 1.1. Here, the output file name is the same as the input level 0 file except for the last 4 characters. In the above example, the user need not know the cycle number because the software first tries cycle number 1 and if needed, increments the cycle number until the file is found, or until a preset maximum is reached. This is the value of icyc_max and is currently set to 5. See the next subsection on routine OPN_L0_FILE_UNIX for more details.

## A.2 Additional Level 0 C Software.

### A.2.1 Level 0 C File Open Function Routine (opn_l0_file_c)

The C function routine opn_l0_file_c (file opn_l0_file_c.c) opens a UARS level 0 file with the proper attributes. It calls gen_l0_name_c (file gen_l0_name_c.c) to generate the file name based on user-input values such as the acronyms for instrument and parameter, the uars day number, and the data version number, which have been described above. The use of this function parallels that for the Fortran version, which is described in Section A.1.1.

Usage:

void opn_l0_file_c(char *instr,int iuars_day,int iver_in,

int icyc_max,int itype_rd,int in_recl,int *icyc,FILE **fp_rd,

char *flname_rd,int *ios_rd);

opn_l0_file_c(instr,iuars_day,iver_in,icyc_max,itype_rd,

in_recl,&icyc,&fp_rd,flname_rd,&ios_rd);

arguement    type    i/0     description

------------------------------------------------------------------------

instr        ch*12   i       instrument acronym.

iuars_day    i*4     i       uars day. (e.g., sept 12, 1991 is

uars day 1, jan 1 1992 is uars

day 112; jan 1 1993 is uars day 478)

iver_in      i*4     i       data version.

icyc_max     i*4     i       maximum cycle number to try.

itype        i*4     i       set last 4 characters of input file

name.

1: prod

2: bnbe

3: bnle

4: asci

in_recl      i*4     i       record length (bytes) of file if fixed

length.

icyc         i*4     i/o     nominally 0 on input.

if 0 on input, routine will assume an

existing file. cycles number will be

incremented from 1 to icyc_max until

success. if existing file is found,

icyc is returned.

ifp          FILE**  o       pointer to file pointer

flname       ch*50   o       flname of file.

ios          i*4     o       status of open.

### A.2.2 Level 0 C File Name Function Routine (gen_l0_name_c)

Function routine gen_l0_name_c (file gen_l0_name_c.c) generates the correct file name based on input values of the instrument and subtype acronyms, the UARS day number, and the file data version. This routine is called only by

opn_l0_file_c.c, and users only need to link this routine.

### A.2.3 Level 0 Sample C Driver and Link Procedure

An example of a driver that uses mcb_readl0_c to read all types of level 0 files is provided and given in file

get_l0_c.c

The command/script file

cclink_get_l0.com

can be used to compile, link, and generate an executable named

get_l0_c.x

For linking, in addition to the sample driver (file get_l0_c.c), the functions mcb_readl0_c (file mcb_readl0_c.c), opn_l0_file_c (file opn_l0_file_c.c), gen_l0_name_c (file gen_l0_name_c.c), swap16_c (file swap16_c.c), swap32_c (file swap32_c.c), and swap64_c (file swap64_c.c) (noted earlier) are needed as well.

Upon running program get_l0_c.x interactively, the following prompt appears on the screen:

ENTER INSTRUMENT NUMBER

1:CLAES,2:HALOE,3:HRDI,4:ISAMS,5:MLS,6:PEM

7:SOLSTICE,8:SUSIMA,9:SUSIMB,10:WINDII,11:ACRIM

12:ENGINEERING,13:SPACECRAFT,14:OBC,15:QUALITY

ENTER UARS DAY

ENTER FIRST DATA RECORD NUMBER, LAST DATA RECORD NUMBER

(-1 FOR BOTH TO DO ALL DATA RECORDS)

DATA VERSION NUMBER

WRITE ASCI FILE (0=NO,1=YES,2=to SCREEN)

SWAP BYTES (0=NO,1=YES)

An example of a user input to this prompt is

4 486 1 3 2 1 1

The different input variables are separated with blanks. As described

in the prompt, the first input, '4', selects an ISAMS file to

open and read. The '486' selects the UARS day to read (there is one file

for each day). Recall that UARS day number 1 is September 12, 1991, and

January 1 1992 corresponds to UARS day 112. The '1 3' selects the first

and last data records wanted (in this case the first 3 records). The

next input, '2', is the file data version number. The next to last input, '1', means that an ASCII output file of selected data will be written. The last input, also '1', is used for big endian computers, and a value of '0' is input for little endian systems.

With the above input, the program will read the first 3 data records of

the level 0 data file named

isams_l0_d0486.v0002_c01_prod

and write a text file named

isams_l0_d0486.v0002_c01_asci

containing certain portions of data from the 3 selected records.

UARS file name conventions have been described in Section 1.1. Here,

the output file name is the same as the input level 0 file except for

the last 4 characters. In the above example, the user need not know the

cycle number because the software first tries cycle number 1 and if

needed, increments the cycle number until the file is found, or until a

preset maximum is reached. This is the value of icyc_max and is currently set to 5. See the previous subsection on routine opn_l0_file_c for more details.

## A.3 Additional Level 1 Fortran Software.

### A.3.1 Level 1 Fortran File Open Routine (opn_l1_file)

The Fortran routine opn_l1_file (file opn_l1_file.for) opens a UARS level 1 file with the proper attributes.  It calls routine gen_l1_name (file gen_l1_name.for) to generate the needed file name based on user-input values such as acronyms for the instrument and parameter, the uars day, and the data version number. Details are the same as described above in Section A.1.1 for the opn_l0_file routine.

An example of using this routine is given by the sample driver get_isams_l1_data_str.for noted above.

Usage:

CALL OPN_L1_FILE(INSTR,PARAM,IUARS_DAY,IVER_IN,

& ICYC_MAX,ITYPE_IN,IN_RECL,ICYC,LUN,FLNAME,IVAR,IDIRECT,IOS)

Argument list description:

ARGUMENT    TYPE    I/0      DESCRITPTION

------------------------------------------------------------------------

INSTR       CH*12   I        INSTRUMENT ACRONYM.

PARAM       CH*12   I        MEASURE PARAMETER.

IUARS_DAY   I*4     I        UARS DAY. (E.G., SEPT 12, 1991 IS

UARS DAY 1, JAN 1 1992 IS UARS

DAY 112; JAN 1 1993 IS UARS DAY 478)

IVER_IN     I*4     I        DATA VERSION NUMBER.

ICYC_MAX    I*4     I        MAXIMUM DATA CYCLE NUMBER TO TRY.

ITYPE_IN    I*4     I        USED TO DETERMINE LAST 4 CHARACTERS

OF FILE NAME:

0 OR 1: PROD

2: BNBE

3: BNLE

4: ASCI

ALSO USED FOR CONVERSION IF

APPLICABLE.

1: NOCONVERSION

2: CONVERT = 'BIG ENDIAN'

3: CONVERT = 'LITTLE ENDIAN'

IN_RECL     I*4     I        RECORD LENGTH (WORDS) OF

FILE IF FIXED LENGTH.

IF VALUE IS GT 0 FILE IS OPENED

WITH RECL KEYWORD SET TO VALUE OF

IN_RECL.

IF VALUE IS ZERO, FILE WILL BE

OPENED WITHOUT RECL KEYWORD, AND

DEFAULT IS USED. FOR VARIABLE RECORDS,

VALUES FOR VMS ARE:

DEFAULTS:SEGMENTED:2048(BYTES)

OTHERS:133

ICYC        I*4     I/O      SHOULD BE NOMINALLY SET TO 0.

IF 0 ON INPUT, ROUTINE WILL

TRY TO OPEN EXISTING FILE. CYCLES

NUMBERS FROM 1 TO ICYC_MAX WIIL BE

TRIED. IF EXISTING FILE IS FOUND,

ICYC IS RETURNED. IF FILE NOT FOUND,

ICYC IS INCREMENTED BY 1 UP TO

ICYC_MAX.

IF NOT ZERO ON INPUT, FILE IS ASSUMED

NOT TO EXIST AND A NEW FILE IS OPENED

USING THE VALUE IF ICYC.

LUN         I*4     I/O      LOGICAL UNIT NUMBER OF FILE.

IF NOT ZERO ON INPUT, THE INPUT VALUE

IS USED TO OPEN THE FILE.

IF ZERO ON INPUT, LUN WILL

BE SET TO 95 (INPUT) IF ICYC IS 0.

AND TO 96 (OUTPUT) IF ICYC IS NOT 0.

FLNAME      CH*50   O        FLNAME OF FILE.

IVAR        I*4     I        IF  O, OPEN FOR FIXED RECORD LENGTH,

AND IS THE CASE FOR MLS.

IF -1, OPEN WITH KEYWORD RECORDTYPE

SET TO 'SEGMENTED'

IF -2, OPEN WITH KEYWORD RECORDTYPE

SET TO 'VARIABLE'

IDIRECT     I*4     I        INPUT 0:SEQUENTIAL ACCESS,1:DIRECT.

DIRECT IS APPLICABLE TO MLS

IOS         I*4     O        STATUS AFTER ATTEMPT TO OPEN.

------------------------------------------------------------------------

### A.3.2 Level 1 Fortran File Name Routine (gen_l1_name)

Routine gen_l1_name (file gen_l1_name.for) generates the correct file name based on user-input values of the instrument and subtype acronyms, the UARS day number, and the file data version number.

This routine is called only by opn_l1_file, and users only need to link this routine.

### A.3.3 Level 1 Sample Fortran Driver and Link Procedure

An example of using FTH_RWLEV1_STR is provided and given in file

get_isams_l1_data_str.for

The file

get_isams_l1_data_str.com

can be used to link and generate an executable named

get_isams_l1_data_str.exe

Upon running program GET_ISAMS_L1_DATA_STR.EXE interactively, the following prompt appears on the screen:

ENTER INSTR,PARAM(LWR CASE,SNGL QUOTES, PARAM IS DATA)

BEGIN UARS DAY,END UARS DAY

ENTER FIRST DATA RECORD NUMBER, LAST DATA RECORD NUMBER

(-1 TO DO ALL DATA RECORDS)

FILE DATA VERSION

FILE TYPE:0:VMS(PROD),1:VMS(.PRO0),2:BIG ENDIAN,3:LITTLE

WRITE SELECTED DATA TO PLOT?[0:NO,1:YES]

An example of a user input to this prompt is

'isams' 'data' 120 120 1 10 12 2 1

The different input variables are separated with blanks. The first string gives the isams instrument acronym, and the second gives the subtype acronym. The '120 120' selects the begin and end UARS days to read (there is one file for each day). Here, only the file for UARS day 120 is processed. UARS day number 1 is September 12, 1991, and January 1 1992 corresponds to UARS day 112. The '1 10' selects the first and last data records wanted (in this case the first 10 records). The  '12' gives the file data version number, and the '2' is used for the file name generation ( big endian). The last input, namely,  '1' chooses the option to write the selected records to a text file for analysis. A '0' does not produce a file.

With the above input, the program will read the header record and the first 10 data records of the level 1 data file named

isams_l1_sdata_d0120.v0012_c01_bnbe

and write a text file named

isams_l1_sdata_d0120.v0012_c01_asci

containing certain portions of data from the 10 selected records.

## A.4 Additional Level 1 C Software.

### A.4.1 Level 1 C File Open Function (opn_l1_file_c)

The C function routine opn_l1_file_c (file opn_l1_file_c.c) opens a UARS level 1 file with the proper attributes.  It calls routine gen_l1_name_c (file gen_l1_name_c.c) to generate the filename based on input values such as acronyms for the instrument (i.e., claes), parameter (i.e., claes), uars day, and the data version number, which have been described previously. Details are the same as described above in Section A.1.1 for the opn_l0_file routine.

Usage:

opn_l1_file_c(char* instr,char* param,int iuars_day,int iver_in,

int icyc_max,int itype_in,int in_recl,int* icyc,FILE** ifp,

char* flname,int* ios)

Argument list description:

argument    type      i/0    description

--------    ----      ---    ----------------------------------------

instr       char[12]  i      instrument acronym.

param       char[12]  i      measure parameter.

iuars_day   int       i      uars day. (e.g., sept 12, 1991 is

uars day 1, jan 1 1992 is uars

day 112; jan 1 1993 is uars day 478)

iver_in     int       i      data version.

icyc_max    int       i      maximum cycle number to try.

itype       int       i      set last 4 characters of input file name.

1: prod

2: bnbe

3: bnle

4: asci

in_recl     int       i      record length (bytes) of file if fixed

length.

icyc        int       i/o    nominally 0 on input.

if 0 on input, routine will assume an

existing file. cycles number will be

incremented from 1 to icyc_max until

success. if existing file is found,

icyc is returned.

ifp         FILE**    o      pointer to file pointer

flname      char[50]  o      flname of file.

ios         int       o      status of open.

### A.4.2 Level 1 C File Name Function (gen_l1_name_c)

The function routine in file gen_l1_name_c.c generates the file name based on input values of the instrument and subtype acronyms, the UARS day number, and the file data version. This routine is called only by opn_l1_file_c.c, and users only need to link this routine.

### A.4.3 Level 1 Sample C Driver and Link Procedure

A sample driver to use the above functions is provided. The file name containing the driver is

get_isams_l1_data_str_c.c

and the compile and link file name is

get_isams_l1_data_str_c.com

Upon executing this file, an executable is created in  file

get_isams_l1_data_str_c.exe

Use of this C program is similar to that for the corresponding Fortran program described earlier.  Details are repeated here for convenience.

Upon running program

get_isams_l1_data_str_c.exe

interactively, the following prompt appears on the screen:

enter instr,param(lwr case,no quotes)

begin uars day,end uars day

enter first data record number, last data record number

(-1 to do all data records)

file data version

file type (0:vms:prod,2:big endian,3:little endian)

write output to plot (0:no,1:yes)

An example of a user input to this prompt is

isams data 120 120 1 10 12 2 1

The different input variables are separated with blanks. The first string gives the isams instrument acronym, the second gives the subtype acronym. The '198 198' select the begin and end UARS days (there is one file for each day) to read. UARS day number 1 is September 12, 1991; January 1 1992 corresponds to UARS day 112. The input  '1 10' selects the first and last data records wanted (in this case the first 10 records). The '12' gives the file data version number, the '2' is used for the file name generation (2 denotes big endian). The last input, namely '1' chooses the option to write the portions of the selected records to a text file for analysis. A '0' does not produce a file.

With the above input, the program will read the header record and the first 10 data records of the level 1 data file named

isams_l1_sdata_d0120.v0012_c01_bnbe

and write a text file  named

isams_l1_sdata_d0120.v0012_c01_asci

containing certain portions of data from the 10 selected records.

## A.5 Additional Level 2 Fortran Software

### A.5.1 Level 2 Fortran File Open Routine (opn_l2_file)

Routine opn_l2_file (file opn_l2_file.for) opens a UARS level 2 file with the proper attributes. It calls routine GEN_L2_NAME to generate the needed filename based on input values such as acronyms for the instrument and parameter, for the uars day number, and the data version number, which have been described above. Details are the same as described above in Section A.1.1 for the opn_l0_file routine.

Usage:

CALL OPN_L2_FILE(INSTR,PARAM,IUARS_DAY,IVER_IN,

&   ICYC_MAX,ITYPE_IN,IN_RECL,ICYC,LUN,FLNAME,IVAR,IDIRECT,IOS)

Argument list description:

ARGUMENT    TYPE   I/0   DESCRITPTION

----------------------------------------------------------------

INSTR       CH*12  I     INSTRUMENT ACRONYM.

PARAM       CH*12  I     MEASURE PARAMETER.

IUARS_DAY   I*4    I     UARS DAY. (E.G., SEPT 12, 1991 IS

UARS DAY 1, JAN 1 1992 IS UARS

DAY 112; JAN 1 1993 IS UARS DAY 478)

IVER_IN     I*4    I     DATA VERSION NUMBER.

ICYC_MAX    I*4    I     MAXIMUM DATA CYCLE NUMBER TO TRY.

ITYPE_IN    I*4    I     USED TO DETERMINE LAST 4 CHARACTERS

OF FILE NAME:

0 OR 1: PROD

2: BNBE

3: BNLE

4: ASCI

ALSO USED FOR CONVERSION IF APPLICABLE.

1: NOCONVERSION

2: CONVERT = 'BIG ENDIAN'

3: CONVERT = 'LITTLE ENDIAN'

IN_RECL     I*4   I      RECORD LENGTH (WORDS) OF

FILE IF FIXED LENGTH.

IF VALUE IS GT 0 FILE IS OPENED

WITH RECL KEYWORD SET TO VALUE OF

IN_RECL.

IF VALUE IS ZERO, FILE WILL BE

OPENED WITHOUT RECL KEYWORD, AND

DEFAULT IS USED. FOR VARIABLE RECORDS,

VALUES FOR VMS ARE:

DEFAULTS:SEGMENTED:2048(BYTES)

OTHERS:133

ICYC        I*4   I/O    SHOULD BE NOMINALLY SET TO 0.

IF 0 ON INPUT, ROUTINE WILL

TRY TO OPEN EXISTING FILE. CYCLES

NUMBERS FROM 1 TO ICYC_MAX WIIL BE

TRIED. IF EXISTING FILE IS FOUND,

ICYC IS RETURNED. IF FILE NOT FOUND,

ICYC IS INCREMENTED BY 1 UP TO

ICYC_MAX.

IF NOT ZERO ON INPUT, FILE IS ASSUMED

NOT TO EXIST AND A NEW FILE IS OPENED

USING THE VALUE IF ICYC.

LUN         I*4   I/O    LOGICAL UNIT NUMBER OF FILE.

IF NOT ZERO ON INPUT, THE INPUT VALUE

IS USED TO OPEN THE FILE.

IF ZERO ON INPUT, LUN WILL

BE SET TO 95 (INPUT) IF ICYC IS 0.

AND TO 96 (OUTPUT) IF ICYC IS NOT 0.

FLNAME      CH*50 O      FLNAME OF FILE.

IVAR        I*4   I      IF  O, OPEN FOR FIXED RECORD LENGTH

IF -1, OPEN WITH KEYWORD RECORDTYPE

SET TO 'SEGMENTED'

IF -2, OPEN WITH KEYWORD RECORDTYPE

SET TO 'VARIABLE'

IDIRECT     I*4   I      INPUT 0:SEQUENTIAL ACCESS,1:DIRECT

IOS         I*4   O      STATUS AFTER ATTEMPT TO OPEN.

-----------------------------------------------------------------------

### A.5.2 Level 2 Fortran File Name Routine (gen_l2_name)

Routine gen_l2_name (file gen_l2_name.for) generates the correct file name based on input values of the instrument and subtype acronyms, the UARS day number, and the file data version number. This routine is called only by OPN_L2_FILE.FOR, and users only need to link this routine.

### A.5.3 Level 2 Sample Fortran  Driver and Link Procedure

The file name of the sample driver is

get_isams_l2_all_str.for

and the link file is given in

get_isams_l2_all_str.com

Execution of the link file produces an executable in file

get_isams_l2_all_str.exe

Upon running the executable interactively, the following prompt appears on the screen:

ENTER INSTR(LWR CASE, IN SNGL QUTS),PARAMETER(SNGL QUTS)

BEGIN UARS DAY,END UARS DAY

ENTER FIRST DATA RECORD NUMBER, LAST DATA RECORD NUMBER

(-1 FOR BOTH TO DO ALL DATA RECORDS)

FILE DATA VERSION,

FILE TYPE(0:VMS .PROD,1:VMS PRO0,-1:PROV,2:BIG ENDIAN,3:LITTLE)

WRITE SELECTED DATA TO PLOT?[0:NO,1:YES]

An example of a user input to this prompt is

'isams' 'o3' 198 198 1 10 12 2 1

The different input variables are separated with blanks. The first string gives the isams instrument acronym, the second gives the subtype acronym. The '198 198' selects the begin and end UARS days to read (there is one file for each day). UARS day number 1 is September 12, 1991; January 1 1992 corresponds to UARS day 112. The '1 10' selects data records  1 to 10 to read. The '12' gives the file data version number, the '2' is used for the file name generation (2 for big endian). The next to last input, namely '1' chooses the option to write the 10 selected records to a  text file for analysis. A '0' does not produce a file.

With the above input, the program will read the level 2  ozone data file named

isams_l2_so3_d0198.v0012_c01_bnbe

and write a text file

isams_l1_so3_d0198.v0012_c01_asci

containing certain portions of data from the selected records.

## A.6 Additional Level 2 C Software

### A.6.1 Level 2 C File Open Code (opn_l2_file_c)

The C function routine opn_l2_file_c (file opn_l2_file_c.c) opens a UARS level 2 file with the proper attributes.  It calls function gen_l2_name_c (file gen_l2_name_c.c) to generate the file name based on input values such as acronyms for the instrument and the parameter, for the uars day number, and the data version number, which have been described above. Details are the same as described above in Section A.1.1 for the opn_l0_file routine.

Usage:

opn_l2_file_c(char* instr,char* param,int iuars_day,int iver_in,

int icyc_max,int itype_in,int in_recl,int* icyc,FILE** ifp,

char* flname,int* ios)

Argument list description:

argument        type	     i/0     description

--------        -----     ---     -----------------------------------

instr           char[12]  i       instrument acronym.

param           char[12]  i       measure parameter.

iuars_day       int       i       uars day. (e.g., sept 12, 1991 is

uars day 1, jan 1 1992 is uars day

112; jan 1 1993 is uars day 478)

iver_in         int       i       data version.

icyc_max        int       i       maximum cycle number to try.

Itype           int       i       set last 4 characters of input file

name.

1: prod

2: bnbe

3: bnle

4: asci

in_recl         int       i       record length (bytes) of file if

fixed length.

icyc            int       i/o     nominally 0 on input.

if 0 on input, routine will assume

an existing file. cycles number

will be incremented from 1 to

icyc_max until success. if existing

file is found, icyc is returned.

ifp             FILE**    o       pointer to file pointer

flname          char[50]  o       flname of file.

ios             int       o       status of open.

### A.6.2 Level 2 C File Name Function (gen_l2_name_c)

Function gen_l2_name_c (file gen_l2_name_c.c) generates the correct file name based on input values of the instrument and subtype acronyms, the UARS day number, and the file data version. This routine is called only by opn_l2_file_c.c, and users only need to link this routine.

### A.6.3 Level 2 Sample C Driver and Link Procedure

A sample driver to use the above functions is provided. The file name of the driver is

get_isams_l2_all_str_c.c

and the compile and link file is given in

get_isams_l2_all_str_c.com

Execution of  the link file produces an executable in file

get_isams_l2_all_str_c.exe

Use of this C program is similar to that for the corresponding Fortran program described earlier. Details are repeated here for convenience.

Upon running the executable interactively, the following prompt appears on the screen:

enter instr,param(lwr case,no quotes)

begin uars day,end uars day

enter first data record number, last data record number

(negative to do all data records)

data version

in file type (def:0:.prod,2:big endian,3:little endian)

write output (0:no,1:yes)

An example of a user input to this prompt is

isams o3 198 198 1 10 12 2 1

The different input variables are separated with blanks. The first string is the isams instrument acronym, the second gives the subtype acronym. The input  '198 198' selects the begin and end UARS days to read (there is one file for each day). UARS day number 1 is September 12, 1991 January 1 1992 corresponds to UARS day 112. The '1 10' selects data records 1 to 10 to read. The '12' is the file data version number, the '2' is used for the file name generation (big endian). The next to last input, namely '1' chooses the option to write the 10 selected records to a text file for analysis. A '0' does not produce a file.

With the above input, the program will read the level 2 ozone data file named

isams_l2_so3_d0198.v0012_c01_bnbe

and write a text file

isams_l1_so3_d0198.v0012_c01_asci

containing certain portions of data from the selected records.